Error table for VAG Com

-------------------------------------------------------------------------------

This table contains:

2200 error numbers/- texts

and additionally

all 85 different error kinds

The error messages are arranged according to error characteristic numbers with 5 digits and from the following ranges:

01 - Engine electronics

02 - Transmission electronics

03 - Brake electronics (ABS/EDS, ASR, ESP)

08 - Climatic/heater electronics

09 - Electronic central electrical connection

12 - Clutch electronics

15 - Airbag

16 - Steering wheel electronics

17 - Instrument panel employment

18 - / standheizung

19 - Diagnostic interface for data bus

22 - All wheel electronics

24 - Drive slip regulation

25 - Going away barrier

26 - Electrical roof manipulation

34 - Level regulation

35 - Zentralverriegelung

36 - Seat adjustment driver's side

37 - Navigation

45 - Interior monitoring

46 - Central module comfort system

55 - Automatic shining width adjustment (xenon)

56 - Radio

65 - Tire pressure monitoring

66 - Seat/mirror adjustment

76 - A park assistance

and some further.......

And for the following vehicles:

Volkswagen: Lupo 6E, 6X; Polo 6N, 9N; Gulf III, gulf IV; Vento; Bora; Trade wind; Phaeton;

Touareg; Sharan; T4 and Beetle

AUDI: 80 B4; 100 C4; A2; A3 8L, S3; A4, S4; A6, S6, S6 plus;

A8 4D, S8; TT, TT roadster; CoupÃ¨, Cabrio Cabriolet; Allroad quattro

Seat: Arosa; Ibiza; Cordoba; Leon; Toledo; Alhambra

Skoda: Fabia; Felicia; Oktavia; Superb

Ford: Galaxy

and further..........

-------------------------------------------------------------------------------

Error characteristic numbers/texts:

00000 no error recognized

00001 braking expensive equipment

00002 transmission expensive equipment

00003 controller

00004 controller for gas operation -J659

00016 actuator floor space/Defrostklappe in the back on the right of -V195

00017 actuator floor space/Defrostklappe at the rear left -V196

00018 actuator cold flap -V197

00019 actuator warm flap -V198

00020 actuator shut-off valve Defrost and Mannanstroemer on the right of -V199

00021 actuator shut-off valve Defrost and Mannanstroemer on the left of -V200

00022 actuator warm flap center console in the back on the right of -V201

00023 actuator warm flap center console at the rear left -V202

00024 actuator cold flap center console in the back on the right of -V203

00025 actuator cold flap center console at the rear left -V204

00026 actuator verteilklappe Defrost or Mannanstroemer on the right of -V205

00027 actuator verteilklappe Defrost or Mannanstroemer on the left of -V206

00028 actuator Design screen on the left of -V207

00029 actuator Design screen center -V208

00030 actuator Design screen on the right of -V209

00031 tracers Defrost at the rear left -E299

00032 tracers Defrost in the back on the right of -E300

00033 tracers outlets in front on the left of -E301

00034 tracers outlets in front center on the left of -E302

00035 tracers outlets in front center on the right of -E303

00036 tracers outlets in front on the right of -E304

00037 tracers for temperature difference floor space/head area -E305

00038 tracers outlet center console at the rear left -E306

00039 tracers outlet center console in the back on the right of -E307

00040 tracers for safety device for children -E318

00041 actuator for indirect ventilation flap -V213

00042 lamp for side marker light on the left of -M43

00043 lamp for side marker light on the right of -M44

00044 control member test group 1 accomplish

00045 control member test group 2 accomplish

00046 engine for stroke nozzle headlamp wash/wipe system, on the left of -V248

00047 engine for stroke nozzle headlamp wash/wipe system, on the right of -V249

00048 temperature sensors heat exchangers on the left of -G306

00049 temperature sensors heat exchangers on the right of -G307

00050 temperature sensors evaporator -G308

00051 temperature sensors floor space at the rear left -G309

00052 temperature sensors floor space in the back on the right of -G310

00053 temperature sensors center console at the rear left -G311

00054 temperature sensors center console in the back on the right of -G312

00055 engine for safety device for children at the rear left -V142

00056 blower engine for temperature sensors inside -V210

00057 actuator shut-off valve b-column and floor space on the right of -V211

00058 relays for heating wiper resting position -J582

00059 clamp 30 for interior lighting

00060 lamps for fog headlights

00061 floor space lights

00062 function requirement chassis

00063 switches for backup lights -F4

00064 actuator for shut-off valve b-column and floor space on the left of -V212

00065 heating element in the floor space at the rear left -Z42

00066 heating element in the floor space in the back on the right of -Z43

00067 consumers 1

00068 consumers 2

00069 engine for safety device for children in the back on the right of -V143

00070 tension starting battery

00071 tracers for fog headlight -E315

00072 tracers for fog tail light -E314

00073 tracers for glove subject -E316

00074 safety device for plug socket 1 -S184

00075 safety device for plug socket 2 -S185

00076 safety device for plug socket 3 -S281

00077 limit switches for windshield wiper -F229

00078 isolating relays 2.Batterie -J7

00079 switches for interior lighting -E317

00080 function requirement sun roof

00081 undervoltage disconnection seat heating

00082 clamp 61 for generator

00083 advance fuel pump

00084 reverse current relays for electrical system battery -J579

00085 reverse current relays for starting battery -J580

00086 relays for parallel connection batteries -J581

00087 clamp 30 for startingrelevant consumers

00088 load monitoring for starting battery

00089 line monitoring for clamp 30 starting battery

00090 supply line clamp 30 starting battery

00091 signal ignition key puts

00092 temperature sensors starting battery -G331

00093 clamp 15 for startingrelevant consumers

00094 engine for zentralverriegelung, door at the rear left, LOCK -V214

00095 engine for zentralverriegelung, door in the back right, LOCK -V215

00096 engine for zentralverriegelung, driver's door-save -V161

00097 engine for zentralverriegelung, passenger door-save -V162

00098 engine for zentralverriegelung, door in the back left-save -V163

00099 engine for zentralverriegelung, door in the back right-save -V164

00100 tracers for support rod, driver's side -E308

00101 tracers for support rod, front seat passenger side -E309

00102 tracers for support rod, at the rear left -E310

00103 tracers for support rod, in the back on the right of -E311

00104 tracers for gas cap unblocking -E319

00105 signal zentralverriegelung SAVE/LOCK driver's side

00106 signal zentralverriegelung SAVE/LOCK front seat passenger side

00107 signal zentralverriegelung SAVE/LOCK at the rear left

00108 signal zentralverriegelung SAVE /LOCK in the back right

00109 lamp for mirror turn signal driver's side -L131

00110 lamp for mirror turn signal front seat passenger side -L132

00111 control lamp for support rod, driver's side -K174

00112 control lamp for support rod, front seat passenger side -K175

00113 control lamp for support rod, at the rear left -K176

00114 control lamp for support rod, in the back on the right of -K177

00115 tracers for telephone connection front seat passenger side -E320

00116 tracers for telephone connection at the rear left -E321

00117 tracers for telephone connection in the back on the right of -E322

00118 tracers for Defrost driver's side -E323

00119 tracers for Defrost front seat passenger side -E324

00120 external warning lamp/door door light driver's side

00121 external warning lamp/door door light front seat passenger side

00122 external warning lamp/door door light at the rear left

00123 external warning lamp/door door light in the back right

00124 line for communication door expensive device tightening assistance driver's side

00125 line for communication door expensive device tightening assistance front seat passenger side

00126 line for communication door expensive device tightening assistance at the rear left

00127 line for communication door expensive device tightening assistance in the back right

00128 control lamp for telephone connection front seat passenger side -K178

00129 lighting for door interior grasp at the rear left -L133

00130 lighting for door interior grasp in the back on the right of -L134

00131 door external grasp lighting/spiegelleuchte driver's side

00132 door external grasp lighting/spiegelleuchte front seat passenger side

00133 door external grasp lighting/spiegelleuchte at the rear left

00134 door external grasp lighting/spiegelleuchte in the back right

00135 givers for wheel acceleration in front on the left of -G337

00136 givers for wheel acceleration in front on the right of -G338

00137 givers for wheel acceleration at the rear left -G339

00138 givers for wheel acceleration in the back on the right of -G340

00139 givers for body acceleration in front on the left of -G341

00140 givers for body acceleration in front on the right of -G342

00141 givers for body acceleration in the back -G343

00142 valve for absorption adjustment in front on the left of -N336

00143 valve for absorption adjustment in front on the right of -N337

00144 valve for absorption adjustment at the rear left -N338

00145 valve for absorption adjustment in the back on the right of -N339

00146 supply voltage for givers for acceleration in front right/at the rear left

00147 supply voltage for givers for acceleration in front left/in the back right

00148 potential transformers for starting battery charge -A15

00149 no tape end programming takes place

00150 plausibility brake booster system

00151 plausibility addr system

00152 controller for windshield wiper motor front seat passenger side -J584

00153 windshield wiper motor driver's side -V216

00154 windshield wiper motor front seat passenger side -V217

00155 communication of controllers driver's side front seat passenger side

00156 control for disk washer pump

00157 clamp X

00158 function requirement Dimmstufe increases

00159 function requirement Dimmstufe reduce

00160 adaptation brake booster

00161 systematical test brake booster

00162 adjustment controller for braking force reinforcement does not take place

00163 controller for braking force reinforcement learns operating points

00164 controller for battery monitoring -J367 in the emergency operation

00165 switches for transmission position P/N

00166 switches for entrance and starting authorization -E415

00167 keys 5

00168 keys 6

00169 keys 7

00170 keys 8

00171 keys 1 not learned

00172 keys 2 not learned

00173 keys 3 not learned

00174 keys 4 not learned

00175 keys 5 not learned

00176 keys 6 not learned

00177 keys 7 not learned

00178 keys 8 not learned

00179 antenna driver's side for entrance and starting authorization -R134

00180 antenna front seat passenger side for entrance and starting authorization -R135

00181 antenna bumper in the back for entrance and starting authorization -R136

00182 antenna trunk for entrance and starting authorization -R137

00183 antenna -1 interior for entrance and starting authorization -R138

00184 control for tracers engine start/stop

00185 control relay for voltage supply clamp 15

00186 control relay for voltage supply clamp 15SV

00187 control relay for voltage supply clamp 75X

00188 control 1 relay for voltage supply clamp 50

00189 control 2 relays for voltage supply clamp 50

00190 sensor for contact, door external grasp driver's side -G415

00191 sensor for contact, door external grasp front seat passenger side -G416

00192 sensor for contact, door external grasp at the rear left -G417

00193 sensor for contact, door external grasp in the back on the right of -G418

00194 ignition key departure barrier

00195 voltage supply for potentiometer inside mirror

00196 potentiometers horizontal for inside mirror -G353

00197 potentiometers vertically for inside mirror -G354

00198 EC mirrors in the inside mirror -Y7

00199 tracers for interior light in front -E326

00200 tracers for interior light in the back -E327

00201 tracers for read light in front -E328

00202 tracers for read light in the back -E329

00203 switches for sun roof -E8

00204 tracers for sun roof -E325

00205 control lamp for garage gate opener -K179

00206 control engines for inside mirrors

00207 heating for givers for air humidity -N340

00208 clamp 30 for glove specialized lighting

00209 clamp 30 for make-up mirrors

00210 control for interior lights in front

00211 control for interior lights in the back

00212 control for reading lights in front left

00213 control for reading lights in front right

00214 control for reading lights at the rear left

00215 control for reading lights in the back right

00216 signal EC mirror light up

00217 supply voltage for givers for air humidity

00218 givers for air humidity -G355

00219 loading level actively

00220 connection to the sun roof

00221 connection to the interior monitoring

00222 connection to the rain sensor

00223 control lamp for givers for vehicle inclination -K188

00224 ejectors for tail bonnet lock stretch

00225 ejectors for tail bonnet lock ease

00226 control lamp for absorption adjustment -K189

00227 tracers for absorption adjustment -E387

00228 tracers for level regulation -E388

00229 refrigerant pressure

00230 switches for transmission position P -F305

00231 wrong engine data set

00232 wrong transmission data record

00233 sensor for automatic distance regulation erfassungsbereich blocks

00234 sensor for automatic distance regulation adjusts

00235 tracers for automatic distance regulation -E357

00236 Antenne2 for interior for entrance and starting authorization -R139

00237 single solenoid valve for ABS in front on the left of -N59

00238 single solenoid valve for ABS in front on the right of -N58

00239 single solenoid valve for ABS at the rear left -N57

00240 single solenoid valve for ABS in the back on the right of -N56

00241 pressure control valve for anti-slip -N238

00242 valve for engine throttling -N237

00243 exhaust brake

00244 supply voltage for ABS valves in front right + at the rear left

00245 supply voltage for ABS valves in front left + in the back right

00246 mass for ABS valves in front right + at the rear left

00247 mass for ABS valves in front left + in the back right

00248 switches for transmission -E206

00249 function feedback automatic controller for circulating air blowers

00250 switches for area enterprise -E207

00251 givers 4 for fuel supply -G393

00252 SBBR light at the rear left

00253 SBBR light in the back right

is missing to 00254 anti-slip attitude

00255 valves for ABS

00256 givers for refrigerant pressure/temperature -G395

00257 intake valve ABS in front on the left of -N101

00258 single solenoid valve 1 -N88

00259 intake valve ABS in front on the right of -N99

00260 single solenoid valve 2 -N89

00261 intake valve ABS in the back -N103

00262 single solenoid valve 3 -N90

00263 transmissions

00264 single solenoid valve 4 -N91

00265 exhaust valve ABS in front on the left of -N102

00266 single solenoid valve 5 -N92

00267 exhaust valve ABS in front on the right of -N100

00268 single solenoid valve 6 -N93

00269 exhaust valve ABS in the back -N104

00270 single solenoid valve 7 -N94

00272 function disconnection by electromagnetic disturbances

00273 intake valve ABS in the back on the right of -N133

00274 intake valve ABS at the rear left -N134

00275 exhaust valve ABS in the back on the right of -N135

00276 exhaust valve ABS at the rear left -N136

00277 in/exhaust valve ABS in front on the left of -N137

00278 main valve ABS -N105

00279 valve 1 for differential lock -N125

00280 valve 2 for differential lock -N126

00281 givers for driving speed -G68

00282 butterfly valve plates -V60

00283 speed pickups in front on the left of -G47

00284 in/exhaust valve ABS in front on the right of -N138

00285 speed pickups in front on the right of -G45

00286 in/exhaust valve ABS at the rear left -N139

00287 speed pickups in the back on the right of -G44

00288 control member for steering column bolting device -N360

00289 in/exhaust valve ABS in the back on the right of -N140

00290 speed pickups at the rear left -G46

00291 Druckschalter-F116/warning contact -F117

00292 hydraulic power supply pressure level

00293 multi-function switches -F125

00294 push button switches 1 for transmission condition

00295 push button switches 2 for transmission condition

00296 kick-down switches -F8

00297 givers for transmission speed -G38

00298 switches for differential lock -E121

00299 program switches -E122

00300 givers for transmission oil temperature -G93

00301 scavenger pump for ABS -V39

00302 relays for single solenoid valves ABS -J106

00303 Funktionswahlschalter-E91

00304 control automatic controller for fresh air blowers

00305 fuel consumption indicator signal

00306 secondary air system zylinder-Reihe 1

00307 secondary air system zylinder-Reihe 2

00308 supply voltage engines sun roof/Rolo sun roof

00309 dosing pump for cleaning agent -V135

00310 temperature sensors 1 for catalyst -G20

00311 tire filler connector

00312 temperature sensors 2 for catalyst -G132

00313 catalyst

00314 two-way valve for recycling of exhaust gases -N161

00315 connection to the Rolo for sun roof

00316 lamps for tail lighting

00317 controller for rear flap -J605

00318 supply voltage for controller for rear flap

00319 engine for rear flap hydraulics -V241

00320 valve for rear flap hydraulics -N346

00321 givers for rear flap hydraulics -G383

00322 switches for deactivation interior monitoring -E267

00323 givers for vehicle inclination -G384

00324 tracers for deactivation giver for vehicle inclination -E360

00325 tracers for back window opening -E361

00326 switches for emergency shut-down theft alarm system -E362

00327 signal sun roof open

00328 control for unblocking back window

00329 control for unblocking rear flap

00330 signal tail wiper interval

00331 signal tail wiper wiping wash

00332 control for tank flap

00333 control for relays for tightening assistance

00334 control heatable back window stage 2

00335 control tail lights

00336 control lighting tail

00337 control lighting driver's door

00338 control lighting passenger door

00339 control lighting door at the rear left

00340 control lighting door in the back right

00341 control rear flap UP

00342 control rear flap TOO

00343 control rear flap lock swing out

00344 control rear flap lock swing

00345 control rear flap lock unlock

00346 control rear flap lock lock

00347 single solenoid valve 8 -N281

00348 single solenoid valve 9 -N282

00349 single solenoid valve 10 -N283

00350 mass feedback of modulation valves

00351 givers for number of revolutions intermediate shaft -G265

00352 clamp 30A

00353 function feedback automatic controller for fresh air blowers

00354 potential transformers windshield heating -A18

00355 actuator for Mannanstroemer in front on the left of -V237

00356 actuator for Mannanstroemer in front on the right of -V238

00357 control automatic controller for circulating air blowers

00358 control for cooling agent stop valve

00359 temperature sensors Mannanstroemer in front on the left of -G385

00360 temperature sensors Mannanstroemer in front on the right of -G386

00361 heating element for additional heating system -Z35

00362 actuator for amount of air flap at the rear left -V239

00363 actuator for amount of air flap in the back on the right of -V240

00364 clamp 15 Slave

00365 line for communication interior monitoring entrance

00366 line for communication interior monitoring exit

00367 absorbers in front left softly

00368 absorbers in front left hard

00369 absorbers in front right softly

00370 absorbers in front right hard

00371 absorbers at the rear left softly

00372 absorbers at the rear left hard

00373 absorbers in the back right softly

00374 absorbers in the back right hard

00375 control issuing window left open

00376 control issuing window left closes

00377 control issuing window right open

00378 control issuing window right closes

00379 clamp 58s

00380 controller for special vehicles -J608

00381 data bus combination instrument

00382 fuzes for Kopfairbag in the back, driver's side -N343

00383 fuzes for Kopfairbag in the back, front seat passenger side -N344

00384 optical data bus

00385 plus exit audio channel for language/telephone

00386 minus exit audio channel for language/telephone

00387 plus exit audio channel for navigation announcements

00388 minus exit audio channel for navigation announcements

00389 headphone exit 1, left channel

00390 headphone exit 1, right channel

00391 headphone exit 2, left channel

00392 headphone exit 2, right channel

00393 display test, black segments

00394 display test, white segments

00395 display test, red segments

00396 display test, green segments

00397 display test, blue segments

00398 finding lighting

00399 lighting function feedback

00400 turn signals, acoustic feedback

00401 acoustic signal generator

00402 heating element for air additional heating system -Z35

00403 engine for sun roof -V1

00404 engine for sun roof, in the back -V146

00405 engine for rollo sun roof -V260

00406 resounding givers for engine for sun roof -G402

00407 resounding givers engine for sun roof, in the back -G403

00408 resounding givers for engine for Rolo sun roof -G404

00409 switches for sun roof, signal of the emergency tracer lines up continuously

00410 preselection signal for sun roof opening

for rollo lines up to 00411 signal of the tracer continuously

00412 comfort CAN_L line

00413 comfort CAN_H line

00414 CAN_L - Line

00415 CAN_H - Line

00416 thermal protection engine for sun roof

00417 central low clay/tone loudspeakers in front on the left of -R101

00418 central low clay/tone loudspeakers in front on the right of -R102

00419 central clay/tone loudspeakers in front on the left of -R103

00420 central clay/tone loudspeakers in front on the right of -R104

00421 central clay/tone loudspeakers at the rear left -R105

00422 central clay/tone loudspeakers in the back on the right of -R106

00423 thermal protection engine for Rolo sun roof

00424 clock control of the givers for a park assistance

00425 function test of the announcements for a park assistance

00426 control lamp for stability program -K155

00427 wiring test of the givers for a park assistance

00428 function test of the givers for a park assistance

00429 announcement for a park assistance in front on the left of -Y13

00430 announcement for a park assistance in front on the right of -Y14

00431 announcement for a park assistance in the back -Y15

00432 supply voltage for announcements and buzzer a park assistance

00433 tracers for a park assistance -E266

00434 givers for a park assistance in front left inside -G332

00435 givers for a park assistance in front right inside -G333

00436 givers for a park assistance at the rear left inside -G334

00437 givers for a park assistance in the back right inside -G335

00438 givers 2 for fuel supply -G169

00439 givers 3 for fuel supply -G237

00440 givers for fuel supply auxiliary tank -G292

00441 givers for schwimmerstand fuel supply auxiliary tank -G293

00442 clamp 87F fuel pump

00443 safety device fuel pump auxiliary tank -S266

00444 control fuel pump auxiliary tank

00445 loss of refrigerant

00446 function restriction by undervoltage

00447 function restriction by overvoltage

00448 citation pump for Haldexkupplung -V181

00449 citation pump on

00450 citation pump out

00451 all wheel clutch separately

00452 all wheel clutch closed

00453 function restriction by temperature rise

00454 all wheel monitoring

00455 controller for entrance and starting authorization at the comfort CAN -J518

00456 controller for entrance and starting authorization -J518

00457 controller for electrical system -J519

00458 controller for battery monitoring -J367

00459 controller, announcement and control unit for information, in front -J523

00460 controller, announcement and control unit for information, in the back -J524

00461 controller for seat adjustment with MEMORY, front seat passenger -J521

00462 controller for seat adjustment with MEMORY, in the back -J522

00463 controller for digital sound-pack -J525

00464 controller with display unit for radio and navigation -J503

00465 controller for telephone/telematics -J526

00466 controller for steering column electronics -J527

00467 TV tV-Tuner -R78

00468 CD-ROM drive assembly -R92

00469 data bus display/Infotainment in the single-wire enterprise

00470 company data bus comfort in the single-wire enterprise

00471 controller for EGD electronically regulated absorption -J250

00472 controller for braking force reinforcement -J539

00473 controller for electrical park/Handbremse-J540

00474 controller for going away barrier -J334

00475 controller for sliding door -J558

00476 controller for fuel pump -J538

00479 controller for remote maintenance central bolting device -J276

00480 controller in the instrument panel employment -J285, at the Infotainment CAN

00481 controller for traffic radio -J559

00482 display unit for TV and video, in the back -R97

00483 controller for air additional heating system

00484 controller for vehicle situation layer -J603

00485 tracers for zentralverriegelung, door external grasp driver's side -E369

00486 tracers for zentralverriegelung, door external grasp front seat passenger side -E370

00487 tracers f.Zentralverriegelung, door external grasp at the rear left -E371

00488 tracers for zentralverriegelung, door external grasp in the back on the right of -E372

00489 givers for leaking out temperature at the rear left -G405

00490 givers for leaking out temperature in the back on the right of -G406

00491 allocation of the speed pickups at the controller examine

00492 body angles of pitch of the controller for level control

00493 ESP Sensoreinheit -G419

00494 ESP Sensoreinheit, wrong construction unit

00495 ESP Sensoreinheit, supply voltage

00496 givers for vehicle level in front

00497 givers for vehicle level in the back

00498 travel writers -G24

00499 announcement for on-board tension -Y11

00500 announcement for oil temperature -Y12

00501 control lamp for oil level -K38

00502 control lamp for going away barrier -K115

00503 control of valves pump/nozzle

00504 valve for pump/nozzle cylinder 1 -N240

00505 valve for pump/nozzle cylinder 2 -N241

00506 valve for pump/nozzle cylinder 3 -N242

00507 valve for pump/nozzle cylinder 4 -N243

00508 valve for pump/nozzle cylinder 5 -N244

00509 valve for pump/nozzle cylinder 6 -N245

00512 resounding givers not on reference mark

00513 givers for engine speed -G28

00514 givers for ignition -G4

00515 resounding givers -G40

00516 throttle idle microswitches -F60

00517 full load switches -F81

00518 butterfly valve potentiometers -G69

00519 givers for suction tube pressure -G71

00520 air mass/amount of air measurers -G70/-G19

00521 CO potentiometers -G74

00522 givers for coolant temperature -G62

00523 givers for intake air temperature -G42

00524 knocking sensor 1 -G61

00525 Lambdasonde -G39

00526 Bremslichtschalter f

00527 givers for suction tube temperature -G72

00528 elevator givers -F96

is missing to 00529 number of revolutions information

00530 butterfly valve placing he/potentiometers -G88

00531 air mass measurers reference tension

00532 supply voltage

00533 idling regulation

00534 givers for oil temperature -G8

00535 first knocking regulation

00536 second knocking regulation

00537 Lambdaregelung

00538 reference tension

00539 givers for fuel temperature -G81

00540 knocking sensor 2 -G66

00541 potentiometers for schieberweg -G99

00542 givers for needle stroke -G80

00543 number of revolutions after maximum exceeded

00544 load pressure after maximum exceeded

00545 engine/transmission electrical connection

00546 data line defectively

00547 pressure control switches for ABS -F137

00548 voltage supply error memory

00549 fuel consumption signal

00550 spraying beginning regulation

00551 catalyst temperature rise

00552 potentiometers for amount of air measurer -G19

00553 air mass measurers -G70

00554 Lambdaregelung 2

00555 Lambdasonde 2 -G108

00556 potentiometers for recycling of exhaust gases -G212

00557 push button switches power steering -F88

00558 adjusting border metering unit lean

00559 adjusting border metering unit fat

00560 recycling of exhaust gases rule difference

00561 mixture adjustment

00562 givers for oil level/oil temperature -G266

00563 announcement for momentary consumption -Y10

00565 operating and display unit for Climatronic in the back -E265

00566 guidance assistance enterprise

00567 control guidance engine

00568 position sensors in the guidance engine

00569 river guidance engine

00570 relays for guidance engine -J509

00571 guidance coupling

00572 givers for guidance position -G268

00573 givers for guidance moment -G269

00575 suction tube pressure

00576 clamp 15

00577 knocking regulation cylinder 1

00578 knocking regulation cylinder 2

00579 knocking regulation cylinder 3

00580 knocking regulation cylinder 4

00581 knocking regulation cylinder 5

00582 knocking regulation cylinder 6

00583 knocking regulation cylinder 7

00584 knocking regulation cylinder 8

00585 temperature sensors for recycling of exhaust gases -G98

00586 regulation recycling of exhaust gases system

00587 adjusting border metering unit

00588 fuzes for Airbag (driver's side) -N95

00589 fuzes 1 for Airbag (front seat passenger side) -N131

00590 fuzes 2 for Airbag (front seat passenger side) -N132

00591 belt switches driver's side -E24

00592 belt switches front seat passenger side -E25

00593 seat contact switches passenger seat -F151

00594 ignition circle Airbag (driver Airbag, front seat passenger Airbag)

00595 Crashdaten stored

00596 short-circuit between valve lines

00597 different wheel number of revolutions impulses

00598 hydraulic/mechanical error

00599 plausibility push button switch/stop light switch

00600 potentiometers -G92 in the actuator -V68 (for temperature flap)

00601 potentiometers -G112 in the actuator -V70

00602 potentiometers -G114 in the actuator -V85

00603 actuator for floor space /Defrostklappe -V85

00604 potentiometers -G113 in the actuator -V71 (for stagnation pressure flap)

00605 two-way valve for freshness and circulating air flap -N63

00606 two-way valve for cooling agent stop valve -N147

00607 OAT indicators -G106

00608 givers for loading condition -G119

00609 ignition exit 1

00610 ignition exit 2

00611 ignition exit 3

00612 ignition exit 4

00613 ignition exit 5

00614 ignition exit 6

00615 ignition exit 7

00616 ignition exit 8

00617 givers for delay left - Airbag -G104

00618 givers for delay right - Airbag -G105

00619 giver inlet left

00620 giver inlet right

00621 valve for pressure reduction -N155

00622 fuel filters drain

00623 ABS/transmission electrical connection

00624 climatic compressor interference

00625 geschwindigkeitssignal

00626 control lamp for time the glow plugs are on -K29

00627 givers for water level -G120

00628 correcting variable monitoring

00629 brake pedal switches -F47

00631 connection air conditioning system - Motronic

00632 connection Climatronic - combination instrument - interface

00633 lines fuzes/givers for delay

00634 pre-resistor for EDS -N159

00635 heating Lambdasonde before catalyst

00636 givers for acceleration in front on the right of -G121

00637 givers for acceleration at the rear left -G122

00638 engine/transmission electrical connection 2

00639 givers for delay -G123

00640 relays for heating Lambdasonde -J278

00641 ATF temperature

00642 transfer valve EDS in front on the right of -N166

00643 exhaust valve EDS in front on the right of -N167

00644 transfer valve EDS in front on the left of -N168

00645 exhaust valve EDS in front on the left of -N169

00646 ABS ASR/engine electrical connection 1

00647 ABS ASR/engine electrical connection 2

00648 heating Lambdasonde after catalyst

00649 in/exhaust valve ABS in the back -N160

00650 clutch pedal switches -F36

00651 lines for ignition circles

00652 course monitoring

00653 plausibility selector lever/transmission

00654 fuzes for belt-taut (driver's side) -N153

00655 fuzes for belt-taut (front seat passenger side) -N154

00656 seat allocation sensor front seat passenger side -G128

00657 actuator for center outlet -V102

00658 service module

00660 kickdown switches/butterfly valve potentiometers

00661 temperature indication

00662 tachometers

00663 speedometers

00664 fuel quantity indication

00665 control lamp for belt warning -K19

00666 gong

00667 outside temperature signal

00668 on-board tension Kl. 30

00670 givers for butterfly valve plate -G127

00671 switches for GRA -E45

00672 hydraulic pump ABS with pre-resistor

00679 heating Lambdasonde 2 before catalyst

00684 heating Lambdasonde 2 after catalyst

00689 wrong air in the air intake system

00694 lighting switch and instruments

00696 valve for pressure-reducing valves on the left of -N170

00697 valve for pressure-reducing valves on the right of -N171

power input increased 00698 controller

00699 Lambdasonde after catalyst -G130

00700 Lambdasonde 2 after catalyst -G131

00702 givers for fuel composition -G133

00703 no-load operation recognition butterfly valve potentiometer/throttle idle microswitch

00705 relays for radiator exhaust stage 1 -J279

00706 relays for radiator exhaust stage 2 -J513

00707 valve for centre outlets -N236

00709 photo sensor 2 for sun exposure -G134

00710 actuator for Defrostklappe -V107

00711 actuator for floor space flap on the left of -V108

00712 actuator for floor space flap on the right of -V109

00713 actuator for center outlets on the left of -V110

00714 actuator for center outlets on the right of -V111

00715 actuator for rear outlet -V112

00716 actuator for circulating air flap -V113

00717 actuator for AKF flap -V114

00718 switches for nozzle left above -F179

00719 switches for nozzle on the top right -F180

00720 switches for nozzle left down -F181

00721 switches for nozzle right down -F182

00722 switches for nozzle center on the left of -F183

00723 switches for nozzle center on the right of -F184

00724 switches for nozzle rear area on the left of -F185

00725 switches for nozzle rear area on the right of -F186

00726 switches for nozzle rear area center -F187

00727 potentiometers -G135 in the actuator -V107 (for Defrostklappe)

00728 potentiometers -G136 in the actuator -V110 (for center outlets left)

00729 potentiometers -G137 in the actuator -V111 (for center outlets right)

00730 potentiometers -G138 in the actuator -V102 (for center outlets)

00731 potentiometers -G139 in the actuator -V108 (for floor space flap left)

00732 potentiometers -G140 in the actuator -V109 (for floor space flap right)

00733 potentiometers -G141 in the actuator -V112 (for rear outlets)

00734 potentiometers in centre outlet -G142

00735 potentiometers -G143 in the actuator -V113 (for circulating air flap)

00736 potentiometers -G144 in the actuator -V114 (for AKF flap)

00737 valve for heating regulation on the left of -N175

00738 valve for heating regulation on the right of -N176

00739 pump for coolant circulation -V50

00740 givers for cylinder 1 recognition -G145

00741 brake pedal monitoring

00742 driving battery ventilation system

00743 givers for battery ventilation -G146

00744 driving battery temperature control

00745 isolation monitoring

00746 driving battery cell loss

00747 givers for battery temperature in front -G52

00748 givers for battery temperature in the back -G53

00749 ventilation flap

00750 error lamp

00751 capacity announcement driving battery

00752 exhausts and battery heating

00753 electrical connections of wheel number of revolutions impulses

00754 hot light

00755 control lamp for oil pressure -K3

00756 givers for leaking out temperature on the left of -G150

00757 givers for leaking out temperature on the right of -G151

00758 secondary air system

00759 adjusters for leaking out temperature on the left of -G155

00760 adjusters for leaking out temperature on the right of -G156

00761 errors in the engine expensive equipment stored

00762 einspritzventil -N181

00763 givers for gas pressure (driver's side) -G147

00764 givers for gas pressure (front seat passenger side) -G148

00765 givers for rule slidegate valve way -G149

00766 givers for leaking out temperature -G152

00767 givers for evaporator temperature in the back -G153

00768 givers for heat exchanger temperature in the back -G154

00769 givers coolant temperature engine exit -G82

00770 givers coolant temperature radiator exit -G83

00771 givers for fuel quantity indication g

00772 oil pressure switches -F22

00773 givers for oil pressure -G10

00774 givers for vehicle level HL -G76

00775 givers for vehicle level HR -G77

00776 givers for vehicle level VL -G78

00777 givers for position of the gas pedal -G79

00778 givers for guidance angle -G85

00779 temperature sensors for outside temperature -G17

00780 givers for vertical acceleration -G90

00781 actuator in front on the left of -V76

00782 actuator in front on the right of -V77

00783 actuator at the rear left -V78

00784 actuator in the back on the right of -V79

00785 temperature sensors - instrument panel -G56

00786 temperature sensors - roof -G86

00787 temperature sensors - fresh air suction port -G89

00788 two-way valve floor space Defrostklappe -N118

00789 switches for reverse movement -F41

00790 freshness/circulating air flap

00791 thermal relays for evaporator -E33

00792 push button switches for air conditioning system -F129

00793 givers for brake pedal position -G100

00794 givers for hydraulic pump -G101

00795 givers for vertical acceleration in the back -G102

00796 blowers for temperature sensor -V42 (instrument panel)

00797 photo sensor for sun exposure -G107

00799 givers for coolant temperature -G110

00800 temperature sensors - fresh air blower -G109

00801 high pressure switches for magnetic clutch -F118

00802 low pressure switches for air conditioning system -F73

00803 givers for spring travel in front on the right of -G116

00804 givers for spring travel in front on the left of -G115

00805 valve for shock strut VL -N148

00806 valve for shock strut VR -N149

00807 valve for shock strut HL -N150

00808 valve for shock strut HR -N151

00809 brake boosters ESP

00810 givers 1/2 (- G201/-G214) for brake pressure

00811 system not query ready

00812 release switches for solenoid coil for brake pressure -F841

00813 givers 2 for brake pressure -G214

00814 solenoid coil for brake pressure -N247

00815 switches for brake recognition -F238

00816 givers for guidance assistance -G250

00817 guidance assistance temperature protection

00818 givers for leaking out temperature evaporator -G263

00819 high pressure givers -G65

00820 switches for brake recognition -F83

00821 antenna 2 for radio -R93

00822 connection of the digital sound package to the radio

00823 LINE exit in front left

00824 control lamp for ASR -K86

00825 heatable driver's seat -Z6

00826 heatable passenger seat -Z8

00827 relays for exhausts for cooling agent -J26

00828 relays for 3-te stage exhaust cooling agent -J135

00829 controller for heating -J162

00830 controller for manipulationmanipulation manipulation -J256

00831 controller for exhausts for cooling agent, stage 1+2 -J293

00832 Bedienungs-und display unit -E87

00833 signal for control heatable windshield

00834 signal for control heatable back window

00835 connection to the controller for manipulationmanipulation manipulation

00836 valve 1 for gangwahl -N284

00837 valve 2 for gangwahl -N285

00838 valve 3 for gangwahl -N286

00839 valve 4 for gangwahl -N287

00840 relays for hydraulic pump transmission -J510

00841 givers for hydraulic pressure transmission -G270

00842 controller for electronic transmission

00843 potentiometers for selector levers forwards/back -G272

00844 switches for lane recognition selector lever -F257

00845 switches for n-recognition selector lever -F258

00846 switches stop recognition selector lever -F259

00847 relays for consumer disconnection -J511

00848 switches for starting/stop enterprise -E262

00849 s-contact at the ignition starting switch D

00850 tax exit active amplifier at the radio

00851 loudspeakers

00852 loudspeakers in front

00853 loudspeakers in the back

00854 exit radio display instrument panel employment

00855 connection to CD change-over switch

00856 antenna at the radio

00857 CD change-over switches -R41

00858 connection ZF exit radio to the antenna amplifier

00859 LINE exit in front right

00860 LINE exit at the rear left

00861 connection to the computer for navigation

00862 antenna for navigation (government inspection department) -R50/-R52

00863 antenna 1 for TV -R55

00864 antenna 2 for TV -R56

00865 antenna 3 for TV -R57

00866 antenna 4 for TV -R58

00867 connection to the ABS controller

00868 angle of rotation sensor -G208

00869 LINE exit in the back right

00870 low clay/tone loudspeakers in front on the left of -R21

00871 low clay/tone loudspeakers in front on the right of -R23

00872 low clay/tone loudspeakers at the rear left -R15

00873 low clay/tone loudspeakers in the back on the right of -R17

00874 hochtonlautsprecher in front on the left of -R20

00875 hochtonlautsprecher in front on the right of -R22

00876 hochtonlautsprecher at the rear left -R14

00877 hochtonlautsprecher in the back on the right of -R16

00878 connections to loudspeakers VL

00879 connections to loudspeakers VR

00880 connections to loudspeakers at the rear left

00881 connections to loudspeakers in the back right

00882 service module for program selection -E200

00883 ignitionstarterswitchingground (clamp S)

00884 ignitionstarterswitchingground (clamp X)

00885 ignitionstarterswitchingground (clamp 50)

00886 turn signal switches -E2

00887 tracers for warning light -E229

00888 windshield wiper switches for interval enterprise -E22

00889 signalhornbetaetigung h

00890 tracers for heatable back window -E230

00891 tracers for remote unblocking, rear flap -E233

00892 tracers for unblocking/rear flap lockcylinder -F248

00893 tracers unblocking/rear flap grasp -E234

00894 tracers for heating outside mirror -E231

00895 GRA/addr operating sector -E45

00896 closing unit rear flap -F256

00897 disk washer pump -V5

00898 control climatic compressor

00899 safety device for wiper engine -S128

00900 safety device horn/double clay/tone horn -S194

00901 backup lights

00902 safety device for remote unblocking, rear flap -S195

00903 safety device for heating, outside mirror -S196

00904 safety device magnet for selector lever barrier -S197

00905 safety device for backup lights -S40

00906 horn/double clay/tone horn -H1

00907 interference load management

00908 controller for wiper engine

00909 windshield wiper motor v (stage 1/2)

00910 control lamp for hazard warning flasher -K6

00911 control lamp heatable back window -K10

00912 switches for window lifter VL -E40

00913 switches for window lifter VR, driver's side -E81

00914 switches for window lifter HL, driver's side -E53

00915 switches for window lifter HR, driver's side -E55

00916 check switches for window lifters in the back -E39

00917 automatic controllers for windshield wiper controlled cycle switching

00918 clamp 31

00919 engine for rear windshield wiper -V12

00920 heatable outside mirrors (Z4/Z5)

00921 control lamp heatable outside mirrors -K153

00922 windshield wiper switches for interval enterprise -E22 (stage 1)

00923 windshield wiper switches for interval enterprise -E22 (stage 2)

00924 relays for headlamp wash/wipe system -J39

00925 safety device (30) for interior lights -S261

00926 clamp 30

00927 clamp 30 right

00928 closing unit for zentralverriegelung driver's side -F220

00929 closing unit for zentralverriegelung front seat passenger side -F221

00930 closing unit for zentralverriegelung HL -F222

00931 closing unit for zentralverriegelung HR -F223

00932 engine window lifter driver's side -V147

00933 engine window lifter front seat passenger side -V148

00934 engine window lifter HL -V26

00935 engine window lifter HR -V27

00936 switches window lifter front seat passenger side -E107

00937 switches window lifter HL -E52

00938 switches window lifter HR -E54

00939 engines mirror adjustment driver's side -V149

00940 engines mirror adjustment front seat passenger side -V150

00941 engine mirror folding driver's side -V121

00942 engine mirror folding front seat passenger side -V122

00943 heatable outside mirror driver's side -Z4

00944 heatable outside mirror front seat passenger side -Z5

00945 Crashsensor for Frontairbag -G190

00946 interior light w

00947 switches remote unblocking rear flap -E188

00948 signal sun roof closes

00949 engine for zentralverriegelung rear flap -V53, LOCK

00950 engine for zentralverriegelung rear flap -V53, UNLOCK

00951 relays for engine remote unblocking rear flap -J398

00952 signal driver's door openly

00953 zeitbegrenzung interior light

00954 interlock relays for starter -J433

00955 keys 1

00956 keys 2

00957 keys 3

00958 keys 4

00959 control lamp zentralverriegelung safe -K133

00960 code switches zentralverriegelung driver's side

00961 code switches zentralverriegelung front seat passenger side

00962 alarm by inclination sensor

00963 signal line to the inclination sensor

00964 signal driver's door openly; Plus

00965 safety device for alarm horn -S158

00966 safety device for turn signals -S151

00967 turn signals left

00968 turn signals right

00969 safety device for heatable back window -S41

00971 relays for heatable windshield -J410

00972 relays for heatable windshield on the right of -J411

00973 switches for heatable back window -E15

00974 switches for heatable windshield -E180

00975 heatable back window -Z1

00976 control lamp for heatable windshield -K122

00977 headlight low beam left + right

00978 lamp for headlight low beam headlights on the left of -M29

00979 lamp for headlight low beam headlights on the right of -M31

00980 safety device for headlight low beam on the left of -S152

00981 safety device for headlight low beam on the right of -S153

00982 safety device for parking light on the left of -S154

00983 safety device for parking light on the right of -S155

00984 lamp for tail light on the left of -M4

00985 lamp for tail light on the right of -M2

00986 safety device for brake lights -S156

00987 lamp for stop light on the left of -M9

00988 lamp for stop light on the right of -M10

00989 safety device for consumer disconnection -S157

00990 consumer disconnection

00991 interior lighting

00992 consumer disconnection actively

00993 consumer disconnection inactively

00994 givers front vertical adjustment driver's seat -G215

00995 givers rear vertical adjustment driver's seat -G216

00996 givers vertical adjustment head restraint driver's seat -G217

00997 engine for adjustment driver's seat -V28

00998 engine for backrest adjustment driver's seat -V45

00999 engine for front vertical adjustment driver's seat -V29

01000 engine for rear vertical adjustment driver's seat -V30

01001 engine for head restraint adjustment driver's seat -V103

01002 tracers front vertical adjustment up, driver's seat -E208

01003 tracers front vertical adjustment off, driver's seat -E209

01004 tracers rear vertical adjustment up, driver's seat -E210

01005 tracers rear vertical adjustment off, driver's seat -E211

01006 tracers adjustment forwards, driver's seat -E212

01007 tracers adjustment back, driver's seat -E213

01008 reference: Emergency stop switch operates! (MEM off switch released -E190)

01009 givers adjustment, driver's seat -G218

01010 givers backrest adjustment, driver's seat -G219

01011 tracers head restraint adjustment up, driver's seat -E214

01012 tracers head restraint adjustment off, driver's seat -E215

01013 climatic compressor load signal

01014 output stage for exhaust thermostat

01015 radiator exhaust price increase

01016 luftablassventil throttle control absorption -N106

01017 compressor for throttle control absorption -V65

01018 exhausts for cooling agent -V7

01019 relays

01020 water pump -V36

01021 control lamp for differential lock -K81

01022 interior light, combination picture activates

01023 buzzers/gong -H3

01024 rain sensor -G213

01025 control error lamp defectively

01026 blowers for evaporators in the back -V20

01027 warm air blowers in the back -V47

01028 relays for blower -J323

01029 relays for air conditioning system -J32

01030 allotting pro rata aster zentralverriegelung driver's side, lock

01031 allotting pro rata aster zentralverriegelung driver's side, unlock

01032 allotting pro rata aster zentralverriegelung front seat passenger side, lock

01033 allotting pro rata aster zentralverriegelung front seat passenger side, unlock

01034 window lifters thermal protection actively, drivers

01035 window lifters thermal protection actively, front seat passengers

01036 window lifters thermal protection actively, HL

01037 window lifters thermal protection actively, HR

01038 zentralverriegelung thermal protection

01039 givers for coolant temperature gauge -G2

01040 ABS/transmission electrical connection 2

01041 ASR function implausibly

01042 controller does not code

01043 controller: wrong software-Version

01044 controller wrongly codes

01045 switches for Tiptronic -F189

01046 control lamp for brake lining -K32

01047 control lamp for Zweikreis-und parking brake plant -K7

01048 control lamp for Diesel electronics -K104

01049 on-board tension Kl. 50

01050 glow plug monitoring

01051 actuator amount of fuel regulation -V117

01052 potentiometers for load signal -G157

01053 valve for beginning of injecting -N182

01054 relays for supply voltage clamp 30 -J317

01055 givers for Kraftstoffoerderbeginn -G158

01056 function: Equalizing charge

01057 function: Tension constant charge

01058 function: Current constant charge

01059 givers for rotor situation of -G159

01060 givers for coil temperature groove reason of -G160

01061 givers for coil temperature end winding -G161

01062 signal for battery power reduction

01063 switches for e-recognition selector lever -F271

01064 clamp 58d - Dimmung interior light

01065 connection RNS to the TV Antennenverstaerker

01066 geschwindigkeitssignal of instrument panel

01067 valve for disconnection 2. Heat exchanger -N317

01068 relays for hydraulic pump clutch plate -J498

01069 pressure system brake booster

01070 relays for starter -J53

01071 givers for clutch way -G162

01072 negative pressure vent for clutch plate -N183

01073 pressure system clutch

01074 ventilation valve for clutch plate -N184

01075 relays for unterdruckpumpe -J318

01076 relays for hydraulic pump clutch -J319

01077 negative pressure switches brake booster -F190

01078 switches for course manipulation -F191

01079 relays for guidance hydraulics -J320

01080 switches power steering systems support -F192

01081 priority switching valve -N185

01082 control lamp for fuel reserve -K105

01083 control lamp for lack of washing water -K106

01084 control lamp for temperature warning 0Â°C -K107

01085 control lamp for temperature warning 4Â°C -K108

01086 givers for speedometer -G22

01087 basic adjustment not accomplished

01088 mixture adjustment 2

01089 switches for clamps put down -F204

01090 switches for clamps raised -F203

01091 switches for verdeck in front -F202

01092 switches for verdeck put down -F171

01093 switches for box covercover box covers above -F201

01094 switches 3 box covercover box cover on the left of -F195

01095 switches of 2 box covercover box covers on the left of -F197

01096 switches 1 box covercover box cover on the left of -F199

-F172 locks 01097 switches for verdeck

01098 switches for rear flap to -F206

01099 switches for trunk locks

01100 switches for trunk unlocks

01101 switches for unblocking barrier -F205

01102 switches 3 box covercover box cover on the right of -F196

01103 switches of 2 box covercover box covers on the right of -F198

01104 switches 1 box covercover box cover on the right of -F200

01105 single solenoid valve 8 -N186

01106 relays for window lifters lower -J291

01107 control light for verdeck -K98

01108 relays for window lifters raise -J292

01109 relays for hydraulic pump -J321

01110 magnet for unblocking barrier -N187

01111 actuator 1 for trunk lock

01112 current supply for actuator 1 and 2

01113 actuator 2 for trunk lock

01114 switches for parking brake control of -F9

01116 actuator for unblockingunblocking unblocking

01117 load signal for generator clamp DF

01118 engine preliminary heating

01119 signal for course recognition

01120 cam shaft adjustment 1

01121 cam shaft adjustment 2

01122 resounding givers 2 -G163

01123 control incorrectly

01124 load time monitoring

01125 suction tube change-over

01126 signal for engine speed

01127 control lamp for fuel reserve -K16

01128 read coil for going away safety device -D2

01129 s-contact -H15

01130 starting from self-service impulse

01131 control turn signals

01132 infrared sensor in front -G166

01133 infrared sensor in the back -G167

01134 alarm horn -H12

01135 sensors for interior monitoring

01136 starters starting interruption

01137 switches for zentralverriegelung; Verriegelungs-Kontakte

01138 switches for zentralverriegelung; Driver's door unblocking

01139 switches for zentralverriegelung; Passenger door unblocking

01140 switches for zentralverriegelung; Rear flap unblocking

01141 switches for rear flap unblocking -E165

01142 engines for zentralverriegelung; Driver's door and tank bolting device too

01143 engines for zentralverriegelung; Driver's door and tank bolting device up

01144 engine for zentralverriegelung; Passenger door open

01145 engine for zentralverriegelung; rear doors open

01146 engine for zentralverriegelung; Passenger door and rear doors too

01147 engine for rear flap bolting device -V120

01148 activation of the Safesicherung doors

01149 deactivation of the Safesicherung doors

01150 analog displays

01151 check switches for diesel engine -F207

01152 switches for course monitoring -F209

01153 switches for Ecomatic -E163

01154 push button switches for coupling system -F210

01155 clutch

01156 switches for course recognition -F208

01157 supply voltage for alarm horn

01158 supply voltage for turn signals

01159 lines for Safesicherung

01160 relays for glow plug cooling agent -J325

01161 output stage cam shaft control valve

01162 burn misfires

01163 ignition copy

01164 ESP enterprise

01165 butterfly valve control unit -J338

01166 signal for engine moment

01167 valve for vollastanschlag -N194

01168 valve for idling speed rise -N177

01169 tuerkontaktschalter driver's side -F2

01170 givers for injecting duration -G175

01171 temperature sensors passenger seat -G60

01172 temperature sensors driver's seat -G59

01173 engine for adjustment driver's seat -V28

01174 engine for vertical adjustment driver's seat -V138

01175 adjusters for heatable driver's seat -E94

01176 keys

01177 engine expensive equipment not entitled

01178 data bus drive, bus peace

01179 key programming wrongly

01180 engine/climatic compressor disconnection - electrical connection

01181 initialization: only 2 keys learned

01182 elevator adaptation

01183 CAT flare

01184 givers for leaking out temperature in the back -G174

01185 fresh air blowers in the back -V80

01186 actuator for air distribution in the back -V136

01187 actuator for temperature flap in the back -V137

01188 controller/magnetic clutch - electrical connection

01189 actuator for air distribution in front -V145

01190 controller/actuators - electrical connection

01191 engines for seat adjustment

01192 clutch for transducer bypass

01193 relays for small amount of heat -J359

01194 relays for large amount of heat -J360

01196 engine/transmission CAN bus

01197 data bus drive wrong software conditions

01198 data bus comfort wrong software conditions

01199 engine/ABS - electrical connection

01200 supply voltage of ABS valves

01201 supply voltage ABS pump

01202 diagnostic line short-circuit

01203 ABS/instrument panel employment - electrical connection

01204 givers for engine temperature -G27

01205 relays for Climatronic -J254

01206 signal for time interval ignition out

01207 controller for additional heating system -J364

01208 data record changes

01209 number of revolutions signal generator clamp W

switching position learns 01210 controller

01211 fuzes for belt-taut in the back driver's side -N196

01212 fuzes for belt-taut in the back front seat passenger side -N197

01213 fuzes for belt-taut in the back center -N198

01214 Crashdaten of belt-taut stored

01215 seat allocation sensor in the back driver's side -G177

01216 seat allocation sensor in the back front seat passenger side -G178

01217 fuzes for Seitenairbag in front driver's side -N199

01218 fuzes for Seitenairbag in front front seat passenger side -N200

01219 fuzes for Seitenairbag in the back driver's side -N201

01220 fuzes for Seitenairbag in the back front seat passenger side -N202

01221 Crashsensor Seitenairbag driver's side -G179

01222 Crashsensor Seitenairbag front seat passenger side -G180

01223 signal zentralverriegelung open

01224 equipment wrongly adjusted

01225 funkempfaenger standheizung -R64

01226 Crashdaten Seitenairbag driver's side stored

01227 Crashdaten Seitenairbag front seat passenger side stored

01228 code switches disconnection Airbag, front seat passenger side -E224

01229 sensor for air humidity, air conditioning system -G260

01230 givers for leaking out temperature floor space on the left of g 261

01231 givers for leaking out temperature floor space on the right of g 262

01232 regulating valve for compressor of the air conditioning system -N280

01233 stop valve for cooling agent, heating -N279

01234 controller for heatable windshield -J505

01235 secondary air injecting valve -N112

01236 magnet for selector lever barrier -N110

01237 fuel turn off valve -N109

01238 firing angle adjustment

01239 ventilation valve butterfly valve plate -N97

01240 bleed valve butterfly valve plate -N117

01241 single solenoid valve 2 for activated charcoal containers -N115

01242 output stages in the controller

01243 valve for register August tubing change-over -N156

01244 controller Lambdasondenheizung -J209

01245 pressure plates -N73

01246 relays for syphon preliminary heating -J81

01247 single solenoid valve 1 for activated charcoal containers -N80

01248 Zweiwegeventil-Vollastanreicherung-N54

01249 einspritzventil cylinder 1 -N30

01250 einspritzventil cylinder 2 -N31

01251 einspritzventil cylinder 3 -N32

01252 einspritzventil cylinder 4 -N33

01253 einspritzventil cylinder 5 -N83

01254 einspritzventil cylinder 6 -N84

01255 einspritzventil cylinder 7 -N85

01256 einspritzventil cylinder 8 -N86

01257 valve for no-load operation stabilization -N71

01258 choke plates -V63

01259 fuel pump relays -J17

01260 valve for schubabschaltung -N65

01261 clock valve for Lambdaregelung -N7

01262 single solenoid valve for load pressure control -N75

01263 cold weather starting valve -N17

01264 relays for secondary tire pump -J299

01265 valve for recycling of exhaust gases -N18

01266 relays for glow plugs -J52

01267 controller for glow automatic timer -J179

01268 mixing plates -N146

01269 valve for beginning of injecting -N108

01270 magnetic clutch for air conditioning system -N25

01271 actuator for temperature flap -V68

01272 actuator for central flap -V70

01273 fresh air blowers -V2

01274 actuator for stagnation pressure flap -V71

01275 code switches disconnection Seitenairbags in the back -E280

01276 hydraulic pump for ABS -V64

01277 relays for hydraulic pump ABS -J185

01278 switching off relays for EDS -J263

01279 givers for longitudinal acceleration -G251

01280 Airbag front seat passenger side is switched off

01281 Airbag driver's side is switched off

01282 transfer valve for suction tube flap -N239

01283 engine for suction tube flap -V157

01284 Seitenairbag driver's side is switched off

01285 Seitenairbag front seat passenger side is switched off

01286 of belt-taut driver's side is switched off

01287 of belt-taut front seat passenger side is switched off

01288 supply voltage Kl. 30

01289 supply voltage Kl. 15

01290 reference tension guidance assistance

01291 code switches disconnection Seitenairbag in the back, driver's side -E295

01292 code switches disconnection Seitenairbag in the back, front seat passenger side -E296

01293 control lamp for Seitenairbag out, in the back driver's side -K167

01294 control lamp for Seitenairbag out, in the back front seat passenger side -K168

01295 controller in the instrument panel employment wrongly codes

01296 givers for leaking out temperature center -G191

01297 givers for leaking out temperature floor space -G192

01299 diagnostic interfaces for data bus

01300 controller for navigation with CD drive assembly -J401

01301 controller for phonetic input -J507

01302 controller for telematics

01303 sending and receiver for telephone

01304 radio

01305 data bus display

01306 fast data bus display

01307 fiber-optic cable data bus display

01308 controller for roof electronics -J528

01309 controller for guidance assistance defectively

01310 controller for level regulation -J197

01311 data bus information

01312 data bus drive defectively

01313 data bus drive in the fail-safe

01314 engine expensive equipment

01315 transmission expensive equipment

01316 braking expensive equipment

01317 controller in the combination instrument

01318 controller for injection pump

01319 controller for longitudinal control -J428

01320 controller for Climatronic -J255

01321 controller for Airbag -J234

01322 controller for multi-functional unit -J501

01323 controller for automatic clutch -J439

01324 controller for all-wheel drive -J492

01325 controller for tire pressure monitoring

01326 controller for multi-function steering wheel -J453

01327 controller for a park assistance

01328 data bus comfort

01329 data bus comfort in the fail-safe

01330 central controller for comfort system -J393

01331 door expensive equipment driver's side -J386

01332 door expensive equipment front seat passenger side -J387

01333 door expensive equipment HL -J388

01334 door expensive equipment HR -J389

01335 controller for seat/mirror position driver

01336 company data bus comfort

01337 door interior grasp lighting

01338 signal doors not closed

01339 door warning lamp

01340 mirror adjustment switches

01341 controller in the instrument panel employment at the comfort CAN -J285

01342 engine expensive equipment 2 (Slave 1)

01343 engine expensive equipment 3 (Slave 2)

01344 gas-discharge lamp

01345 central module for gas-discharge lamp

01346 line to the ignition module

01347 line to the gas-discharge lamp

01348 control lamp for interior monitoring disconnection -K162

01349 alarm by sensor for theft alarm system in front

01350 alarm by sensor for theft alarm system in the back

01351 line for communication on mass

01352 line for clock pulse in front, 5V level

01353 line for clock pulse in the back, 5V level

01354 enabling signal going away barrier

01355 signal; All windows open

01356 signal; All windows and sliding issuing roof close

01357 engine for gas cap bolting device -V155

01358 switches for support rod driver's side -E150

01359 switches for support rod front seat passenger side -E198

01360 switches for theft alarm system open

01361 switches for theft alarm system close

01362 switches for rear flap close -F124

01363 switches for zentralverriegelung, driver's door -F59

01364 switches for zentralverriegelung, passenger door -F114

01365 LOCK/UNLOCK switch/bolting device tracer inside

01366 opening by Crash signal

01367 disconnection of the pump for zentralverriegelung

01368 alarm by switch trunk

01369 alarm by switch hood

01370 alarm by interior monitoring

01371 alarm by tuerkontaktschalter driver's side

01372 alarm by tuerkontaktschalter in the back/front seat passenger side

01373 alarm by earth bar radio

01374 alarm by clamp 15

01375 valves for engine storage stage 1

01376 number of revolutions signal for injection pump

01377 ultrasonic sensor left for theft alarm system -G170

01378 ultrasonic sensor right for theft alarm system -G171

01379 switches for interior monitoring -E183

01380 alarm by sensor for theft alarm system at the rear left

01381 alarm by sensor for theft alarm system in the back right

01382 alarm by sensor for theft alarm system in front left

01383 alarm by sensor for theft alarm system in front right

01384 alarm by glass break sensor

01385 control lamp for alarm installation -K95

01387 line for voltage supply

01388 line for clock pulse

01389 switches for rear flap open -F124

01393 givers for level regulation -G84

01394 control lamp for level regulation -K134

01395 engine for compressor level regulation -V66

01396 valves for rear suspension struts -N150/-N151

01397 solenoid drip valve level regulation -N111

01398 signal line of zentralverriegelung: Doors up

01399 relays for compressor level regulation -J403

01400 level regulation

01402 data line of navigation

01403 glass break sensors in the back

01404 valves for engine storage stage 2

01405 valve 2 for recycling of exhaust gases -N213

01406 no flaming formation

01407 flaming abort

01408 disconnection by undervoltage (fixed value)

01409 repeated flaming abort

01410 heater overheats

01411 temperature sensors -G18

01412 glow plug with Flammwaechter-Q8

01413 dosing pump -V54

01414 combustion air blowers -V6

01415 circulation pump -V55

01416 signal for control fresh air blower

01422 hydraulic pump for FDR -V156

01423 sensor for transverse acceleration -G200

01424 givers for turning rate -G202, signal line

01425 givers for turning rate -G202, reference line

01426 control unit in the steering wheel -E221

01434 relays for stop light suppression ESP -J508

01435 givers 1 for brake pressure -G201

01437 rule situation not learned

01440 fuel level signal

01441 givers for lack of fuel -G210

01442 misfires by lack of fuel

01443 adjustment at battery does not take place

01444 disconnection by undervoltage (AUTOMATIC)

01445 givers for adjustment, driver's seat -G227

01446 givers for backrest adjustment, driver's seat -G230

01447 givers for vertical adjustment, driver's seat -G231

01448 givers for neigungsverstellung, driver's seat -G232

01449 switches for neigungsverstellung driver's seat -E222, back

01450 switches for neigungsverstellung driver's seat -E222, forwards

01451 switches for along and vertical adjustment -E61, up

01452 switches for along and vertical adjustment -E61, off

01453 switches for along and vertical adjustment -E61, forwards

01454 switches for along and vertical adjustment -E61, back

01455 switches for backrest adjustment -E96, forwards

01456 switches for backrest adjustment -E96, back

01457 signal at mirror/steering column controller

01458 signal of zentralverriegelung

01459 tracers drivers 1/MEMORY seat -E218

01460 tracers drivers 2/MEMORY seat -E219

01461 tracers drivers 3/MEMORY seat -E220

01464 givers for brake pressure/transverse acceleration

01482 engines for zentralverriegelung

01483 control tail cover remote unblocking

01484 allotting pro rata aster zentralverriegelung lock

01485 allotting pro rata aster zentralverriegelung unlock

01486 system function test activates

01488 givers for coolant temperature, heating -G241

01489 overheat thermoresistors -G189

01490 automatic flame guards -G64

01491 glow plug for heating -Q9

01492 function barrier

01522 control listeners for telephone -R37

01523 microphone for telephone -R38

01526 tracers for emergency call -E276

01527 tracers for breakdown call -E275

01528 auxiliary antenna for telematics -R90

01529 auxiliary loudspeakers for telematics -R91

01531 stand-by battery

01532 signal line to the combination instrument

01533 searchlight beam Kl.56

01534 control actuator for shining width regulation on the left of -V48

01535 control actuator for shining width regulation on the right of -V49

01537 givers for vehicle level - supply voltage

01539 headlights were not adjusted

01542 givers for turning rate -G202

01543 buzzers for a park assistance -H15

01544 function announcement

01545 givers for a park assistance, at the rear left -G203

01546 givers for a park assistance, at the rear left, center -G204

01547 givers for a park assistance, in the back right, center -G205

01548 givers for a park assistance, in the back on the right of -G206

01549 supply voltage for giver a park assistance

01550 signal for reverse gear

01557 contact switches in the lockcylinder driver's side -F241 open

01558 contact switches in the lockcylinder driver's side -F241 close

01559 driver's door lock

01560 passenger door lock

01561 door lock HL

01562 door lock HR

01563 switches for support rod driver's side -E150, LOCK

01564 switches for Innenverr. Driver's side -E150, UNLOCK

01565 luggage compartment light -W3

01566 signal for interior monitoring activate

01568 signal comfort opening

01569 signal comfort locking

01570 turn-off delay Kl. 15

01571 signal for seat MEMORY

01572 alarm by tuerkontaktschalter front seat passenger side side

01573 alarm by tuerkontaktschalter HL

01574 alarm by tuerkontaktschalter HR

01575 regulation switched off

01577 disconnection by temperature rise

01578 indicator light for Airbag out, front seat passenger side -K145

01581 wrong construction unit recognized

01582 signal for coolant temperature

01585 contact switches in the lockcylinder front seat passenger side -F242, open

01586 contact switches in the lockcylinder front seat passenger side -F242, close

01588 fuzes for Kopfairbag driver's side -N251

01589 fuzes for Kopfairbag front seat passenger side -N252

01592 sensor for air quality -G238

01593 heatable windshield -Z2

01594 controller wrong chassis number

01596 actuator for fresh air/circulating air flap -V154

01613 relays for pump fuel cooling

01625 buzzers for a park assistance in front -H22

01626 givers for a park assistance, in front on the right of -G252

01627 givers for a park assistance, in front right, center -G253

01628 givers for a park assistance, in front left, center -G254

01629 givers for a park assistance, in front on the left of -G255

01638 Crashsensor Seitenairbag driver's side in the back -G256

01639 Crashsensor Seitenairbag front seat passenger side in the back -G257

01646 Kopfairbag driver's side is switched off

01647 Kopfairbag front seat passenger side is switched off

01656 Crashsignal

01686 controller for radiator exhaust oh run -J138

01695 givers 2 for fuel temperature -G248

01719 givers for adjustment, passenger seat -G278

01720 givers for backrest adjustment, passenger seat -G279

01721 givers for rear vertical adjustment, passenger seat -G280

01722 givers for front vertical adjustment, passenger seat -G281

01724 switches for adjustment, passenger seat -E64, forwards

01725 switches for adjustment, passenger seat -E64, back

01726 switches for backrest adjustment, Beifahrersitz-E98, forwards

01727 switches for backrest adjustment, passenger seat -E98, back

01728 switches for rear vertical adjustment, passenger seat -E66, up

01729 switches for rear vertical adjustment, passenger seat E66, off

01730 switches for front vertical adjustment, passenger seat -E65, up

01731 switches for front vertical adjustment, passenger seat -E65, off

01748 switches for Tiptronic in the steering wheel, highly

01749 switches for Tiptronic in the steering wheel, down

01767 givers for vehicle level left

01768 givers for vehicle level right

01769 givers for vehicle level VR -G289

01770 givers for compressor temperature -G290

01771 controller for shining width regulation

01772 signal line of pressure transducer -G291

01773 valve for accumulator -N311

01774 controller for shining width regulation, supply -J431

01775 signal line to the controller for shining width regulation -J431

01776 control unit for level regulation -E281 defectively

01777 redundant signalpfad of control unit for level regulation -E281

01780 givers for vehicle level

01781 extreme vehicle inclined conditions

01796 telematics SIM map

01809 actuator for temperature flap on the left of -V158

01810 actuator for temperature flap on the right of -V159

01836 compressor switched off

01841 potentiometers -G220 in the actuator -V158 (for temperature flap left)

01842 potentiometers -G221 in the actuator -V159 (for temperature flap right)

16397 bank 1, cam shaft adjustment discharge opening malfunctioning

16407 bank 2, cam shaft adjustment discharge opening malfunctioning

16485 air mass measurers -G70 implausible signal

16486 air mass measurers signal too small

16487 air mass measurers signal too largely

16490 suction tube pressure/air pressure -G71/-F96 implausible signal

16491 suction tube pressure/air pressure -G71/-F96 signal too small

16496 intake air temperature signal too small

16497 intake air temperature signal too largely

16500 givers for coolant temperature -G62 implausible signal

16501 givers for coolant temperature -G62 signal too small

16502 givers for coolant temperature -G62 signal too largely

16504 givers for coolant temperature -G62 of electrical errors in the electric circuit

16505 butterfly valve potentiometers implausible signal

16506 butterfly valve potentiometers signal too small

16507 butterfly valve potentiometers signal too largely

16514 bank 1, probe 1 electrical error in the electric circuit (malfunctioning)

16515 bank 1, probe 1 tension too small

16516 bank 1, probe 1 tension too largely

16517 bank 1, probe 1 signal too slowly

16518 bank 1, probe 1 no activity

16519 bank 1, probe 1 heizstromkreis electrical error in the electric circuit

16520 bank 1, probe 2 electrical error in the electric circuit

16521 bank 1, probe 2 tension too small

16522 bank 1, probe 2 tension too largely

16523 bank 1, probe 2 signal too slowly

16524 bank 1, probe 2 no activity

16525 bank 1, probe 2 heizstromkreis electrical error in the electric circuit

16534 bank 2, probe 1 electrical error in the electric circuit (malfunctioning)

16535 bank 2, probe 1 tension too small

16536 bank 2, probe 1 tension too largely

16537 bank 2, probe 1 signal too slowly

16538 bank 2, probe 1 no activity

16540 bank 2, probe 2 electrical error in the electric circuit

16541 bank 2, probe 2 tension too small

16542 bank 2, probe 2 tension too largely

16543 bank 2, probe 2 signal too slowly

16544 bank 2, probe 2 no activity

16554 bank 1, fuel calculation system malfunctioning

16555 bank 1, fuel calculation system system too lean

16556 bank 1, fuel calculation system system too fat

16557 bank 2, fuel calculation system malfunctioning

16558 bank 2, fuel calculation system system too lean

16559 bank 2, fuel calculation system system too fat

16576 givers for fuel pressure -G247 short-circuit after mass

16581 givers for oil temperature -G8 signal too small

16582 givers for oil temperature -G8 signal too largely

16585 einspritzventil Zyl. 1 -N30 of electrical errors in the electric circuit

16586 einspritzventil Zyl. 2 -N31 of electrical errors in the electric circuit

16587 einspritzventil Zyl. 3 -N32 of electrical errors in the electric circuit

16588 einspritzventil Zyl. 4 -N33 of electrical errors in the electric circuit

16593 einspritzventil Zyl. 9 -N299 of electrical errors in the electric circuit

16594 einspritzventil Zyl. 10 -N300 of electrical errors in the electric circuit

16595 einspritzventil Zyl. 11 -N301 of electrical errors in the electric circuit

16596 einspritzventil Zyl. 12 -N302 of electrical errors in the electric circuit

16603 maximum engine speed exceeded

16606 angle sensors 2 for butterfly valve drive -G188 signal too small

16607 angle sensors 2 for butterfly valve drive -G188 signal too largely

16611 givers for position of the gas pedal -G79 signal too small

16612 givers for position of the gas pedal -G79 signal too largely

16620 givers for load pressure -G31 implausible signal

16621 givers for load pressure -G31 signal too small

16622 givers for load pressure -G31 signal too largely

16646 einspritzventil Zyl. 1 -N30 short-circuit after pluses

16649 einspritzventil Zyl. 2 -N31 short-circuit after pluses

16652 einspritzventil Zyl. 3 -N32 short-circuit after pluses

16655 einspritzventil Zyl. 4 -N33 short-circuit after pluses

16669 einspritzventil Zyl. 9 -N299 short-circuit after mass

16670 einspritzventil Zyl. 9 -N299 short-circuit after pluses

16672 einspritzventil Zyl. 10 -N300 short-circuit after mass

16673 einspritzventil Zyl. 10 -N300 short-circuit after pluses

16675 einspritzventil Zyl. 11 -N301 short-circuit after mass

16676 einspritzventil Zyl. 11 -N301 short-circuit after pluses

16678 einspritzventil Zyl. 12 -N302 short-circuit after mass

16679 einspritzventil Zyl. 12 -N302 short-circuit after pluses

16684 burn misfires recognized

16685 Zyl. 1 burn misfire recognized

16686 Zyl. 2 burn misfires recognized

16687 Zyl. 3 burn misfire recognized

16688 Zyl. 4 burn misfires recognized

16689 Zyl. 5 burn misfires recognized

16690 Zyl. 6 burn misfires recognized

16691 Zyl. 7 burn misfires recognized

16692 Zyl. 8 burn misfires recognized

16693 Zyl. 9 burn misfires recognized

16694 Zyl. 10 burn misfires recognized

16695 Zyl. 11 burn misfire recognized

16696 Zyl. 12 burn misfires recognized

16705 givers for engine speed -G28 implausible signal

16706 givers for engine speed -G28 no signal

16708 knocking regulation malfunctioning

16709 knocking sensor 1 -G61 of electrical errors in the electric circuit

16710 knocking sensor 1 -G61 implausible signal

16711 knocking sensor 1 -G61 signal too small

16712 knocking sensor 1 -G61 signal too largely

16716 knocking sensor 2 -G66 signal too small

16717 knocking sensor 2 -G66 signal too largely

16719 givers for engine speed -G28 malfunctioning

16721 crankshaft position sensor signal too small

16724 cam shaft position sensor -G40 malfunctioning

16725 cam shaft position sensor -G40 implausible signal

16726 cam shaft position sensor -G40 signal too small

16727 cam shaft position sensor -G40 signal too largely

16730 cam shaft position sensor -G163 implausible signal

16735 ignition control Zyl. 1 malfunctioning

16736 ignition control Zyl. 2 malfunctioning

16750 cam shaft position sensor -G300 implausible signal

16764 glow plug -Q6 of electrical errors in the electric circuit

16775 cam shaft position sensor -G301 implausible signal

16785 recycling of exhaust gases system throughput too small

16786 recycling of exhaust gases system throughput too largely

16787 valve for recycling of exhaust gases -N18 malfunctioning

16788 recycling of exhaust gases system rule difference

16791 potentiometers for recycling of exhaust gases -N212 signal too small

16792 potentiometers for recycling of exhaust gases -N212 signal too largely

16795 secondary air system flow incorrectly

16804 bank 1, catalyst system effect too small

16805 Vorkatalysator bank 1, effect too small

16806 bank 1, main catalyst effect too small

16814 bank 2, catalyst system effect too small

16815 Vorkatalysator bank 2, effect too small

16816 bank 2, main catalyst effect too small

16825 tank ventilation system throughput incorrectly

16827 tank ventilation system of electrical errors in the electric circuit

16845 Kraftstoffuellstandssignal implausible signal

16885 vehicle speed signal implausible signal

16887 vehicle speed signal signal too largely

16890 idling regulation number of revolutions under desired value

16891 idling regulation number of revolutions over desired value

16894 throttle idle microswitches -F60 malfunctioning

16896 idling speed influence not possible

16916 pressure sensor for air conditioning system signal too small

16917 pressure sensor for air conditioning system signal too largely

16944 voltage supply implausible signal

16946 voltage supply tension too small

16947 voltage supply tension too largely

16952 switches for GRA -E45 implausible signal

16955 stop light switches f implausible signal

16985 controller defectively

16987 controller defectively

16988 controller defectively

16989 controller defectively

16990 controller defectively

16991 butterfly valve control unit -J338 undervoltage during basic adjustment

17022 butterfly valve control unit -J338 implausible signal

17069 main relays -J271 interruption

17070 main relays -J271 short-circuit after mass

17071 main relays -J271 short-circuit after pluses

17086 controller defectively

17087 stop light switches f of electrical errors in the electric circuit

17090 drive position sensor -F125 implausible signal

17094 givers for transmission oil temperature -G93 of electrical errors in the electric circuit

17095 givers for transmission oil temperature -G93 implausible signal

17096 givers for transmission oil temperature -G93 signal too small

17097 givers for transmission oil temperature -G93 signal too largely

17100 givers for transmission entrance number of revolutions -G182 implausible signal

17101 givers for transmission entrance number of revolutions -G182 no signal

17105 givers for transmission output speed -G195 implausible signal

17106 givers for transmission output speed -G195 no signal

17110 number of revolutions signal of the engine expensive equipment implausible signal

17111 number of revolutions signal of the engine expensive equipment no signal

17114 course/translation monitoring wrong speed ratio

17115 1. Course wrong speed ratio

17116 2. Course wrong speed ratio

17117 3. Course wrong speed ratio

17118 4. Course wrong speed ratio

17119 5. Course wrong speed ratio

17125 clutch for transducer bypass no power transmission

17134 switching valve 1 single solenoid valve 1 -N88 malfunction

17135 switching valve 1 single solenoid valve 1 -N88 interruption/short-circuit after mass

17136 switching valve 1 single solenoid valve 1 -N88 short-circuit after pluses

17137 switching valve 1 single solenoid valve 1 -N88 of electrical errors in the electric circuit

17140 switching valve 2 single solenoid valve 2 -N89 interruption/short-circuit after mass

17141 switching valve 2 single solenoid valve 2 -N89 short-circuit after pluses

17142 switching valve 2 single solenoid valve 2 -N89 of electrical errors in the electric circuit

17145 switching valve 3 single solenoid valve 3 -N90 interruption/short-circuit after mass

17146 switching valve 3 single solenoid valve 3 -N90 short-circuit after pluses

17147 switching valve 3 single solenoid valve 3 -N90 of electrical errors in the electric circuit

17418 einspritzventil Zyl.9 -N299 interruption

17419 einspritzventil Zyl. 10 -N300 interruption

17420 einspritzventil Zyl. 11 -N301 interruption

17421 einspritzventil Zyl. 12 -N302 interruption

17428 fuel pressure control rule border exceeded

17433 regulating valve for fuel pressure -N276 of mechanical errors

17463 bank 1, cam shaft adjustment discharge opening short-circuit after pluses

17464 bank 1, cam shaft adjustment discharge opening short-circuit after mass

17465 bank 1, cam shaft adjustment discharge opening interruption

17466 bank 2, cam shaft adjustment discharge opening short-circuit after pluses

17467 bank 2, cam shaft adjustment discharge opening short-circuit after mass

17468 bank 2, cam shaft adjustment discharge opening interruption

17471 fuel pressure control rule border fell below

17472 fuel pressure system of mechanical errors

17473 fuel pressure control rule difference

17481 air mass measurers 2 -G246 signal too small

17482 air mass measurers 2 -G246 signal too largely

17483 Lambda regulation exhaust bank 3 system too lean

17484 Lambda regulation exhaust bank 3 system too fat

17485 Lambda regulation exhaust bank 4 system too lean

17486 Lambda regulation exhaust bank 4 system too fat

17487 Lambda regulation exhaust bank 3 implausible control value

17488 Lambda regulation exhaust bank 4 implausible control value

17489 exhaust bank 3, mixture adaptation range 1 lean border fell below

17490 exhaust bank 3, mixture adaptation range 2 lean border fell below

17491 exhaust bank 3, mixture adaptation range 1 fat border exceeded

17492 exhaust bank 3, mixture adaptation range 2 fat border exceeded

17493 exhaust bank 4, mixture adaptation range 1 lean border fell below

17494 exhaust bank 4, mixture adaptation range 2 lean border fell below

17495 exhaust bank 4, mixture adaptation range 1 fat border exceeded

17496 exhaust bank 4, mixture adaptation range 2 fat border exceeded

17497 bank 2, mixture adaptation range 1 lean border fell below

17499 bank 2, mixture adaptation range 1 fat border exceeded

17509 bank 1, probe 1 tension too small/leakage air

17510 bank 1, probe 1 heizstromkreis short-circuit after pluses

17511 bank 1, probe 1 heizstromkreis achievement too small

17513 bank 1, probe 2 heizstromkreis short-circuit after pluses

17514 bank 2, probe 1 tension too small/leakage air

17515 bank 2, probe 1 heizstromkreis short-circuit after pluses

17516 bank 2, probe 1 heizstromkreis achievement too small

17518 bank 2, probe 2 heizstromkreis short-circuit after pluses

17519 Lambda regulation (bank 1) system too lean

17520 Lambda regulation (bank 1) system too fat

17521 bank 1, probe 1 internal resistance too largely

17522 bank 1, probe 2 internal resistance too largely

17523 bank 1, probe 1 heizstromkreis short-circuit after mass

17524 bank 1, probe 1 heizstromkreis interruption

17525 bank 1, probe 2 heizstromkreis short-circuit after mass

17526 bank 1, probe 2 heizstromkreis interruption

17527 bank 2, probe 1 heizstromkreis short-circuit after mass

17528 bank 2, probe 1 heizstromkreis interruption

17529 bank 2, probe 2 heizstromkreis short-circuit after mass

17530 bank 2, probe 2 heizstromkreis interruption

17535 bank 1, mixture adaptation (mult.) System too fat

17536 bank 1, mixture adaptation (mult.) System too lean

17537 bank 2, mixture adaptation (mult.) System too fat

17538 bank 2, mixture adaptation (mult.) System too lean

17539 bank 2, probe 1 internal resistance too largely

17540 banks 1+2, probe 1 heizstromkreis short-circuit after pluses

17541 banks 1+2, probe 1 heizstromkreis of electrical errors

17544 bank 1, mixture adaptation (ADD.) System too lean

17545 bank 1, mixture adaptation (ADD.) System too fat

17546 bank 2, mixture adaptation (ADD.) System too lean

17547 bank 2, mixture adaptation (ADD.) System too fat

17548 bank 2, probe 2 internal resistance too largely

17549 vice version implausible value

17551 vice version border exceeded

17552 air mass measurers -G70 interruption/short-circuit after mass

17553 air mass measurers -G70 short-circuit after pluses

17554 air mass measurers -G70 supply voltage

17555 Lambda regulation bank 2 system too lean

17556 Lambda regulation bank 2 system too fat

17557 Lambda regulation bank 1 implausible control value

17558 Lambda regulation bank 2 implausible control value

17559 bank 1, mixture adaptation range 1 lean border fell below

17560 bank 1, mixture adaptation range 2 lean border fell below

17563 givers for suction tube pressure -G71 short-circuit after pluses

17564 givers for suction tube pressure -G71 interruption/short-circuit after mass

17565 givers for suction tube pressure -G71 supply voltage

17566 givers for suction tube pressure -G71 implausible signal

17567 signal air mass measurer 1/air mass measurer 2 implausible relationship

17568 givers for suction tube temperature -G72 short-circuit after mass

17569 givers for suction tube temperature -G72 interruption/short-circuit after pluses

17570 givers for fuel temperature -G81 short-circuit after mass

17571 givers for fuel temperature -G81 interruption/short-circuit after pluses

17572 givers for fuel temperature -G81 implausible signal

17573 bank 1, mixture adaptation range 1 fat border exceeded

17574 bank 1, mixture adaptation range 2 fat border exceeded

17575 air mass measurers 2 -G246 implausible signal

17576 air mass measurers 2 -G246 interruption/short-circuit after mass

17577 air mass measurers 2 -G246 short-circuit after pluses

17578 air mass measurers 2 -G246 supply voltage

17579 angle sensors 2 for butterfly valve drive -G188 implausible signal

17580 angle sensors 2 for butterfly valve drive -G188 signal too small

17581 angle sensors 2 for butterfly valve drive -G188 signal too largely

17582 bank 1, fuel calculation system deviation of the durations of injection

17584 bank 1, Lambdakorrektur behind Kat rule border reaches

17585 bank 2, Lambdakorrektur behind Kat rule border reaches

17586 linear Lambda probe pumping Rome interruption

17587 linear Lambdasonde/ pumping Rome short-circuit after mass

17588 linear Lambdasonde/ pumping Rome short-circuit after pluses

17589 linear Lambdasonde/ reference tension interruption

17590 linear Lambdasonde/ reference tension short-circuit after mass

17591 linear Lambdasonde/ reference tension short-circuit after pluses

17598 linear Lambdasonde/ reference tension implausibly

17600 givers for fuel pressure -G247 supply voltage

17601 givers for fuel pressure -G247 interruption/short-circuit after pluses

17602 regulating valve for fuel pressure -N276 short-circuit after pluses

17603 regulating valve for fuel pressure -N276 interruption/short-circuit after mass

17604 bank 1, probe 1 heizstromkreis of electrical errors

17605 bank 2, probe 1 heizstromkreis of electrical errors

17606 bank 1, probe 2 heizstromkreis of electrical errors

17607 bank 2, probe 2 heizstromkreis of electrical errors

17609 einspritzventil Zyl.1 -N30 electrical error in the electric circuit

17610 einspritzventil Zyl.2 -N31 electrical error in the electric circuit

17611 einspritzventil Zyl.3 -N32 electrical error in the electric circuit

17612 einspritzventil Zyl.4 -N33 electrical error in the electric circuit

17613 einspritzventil Zyl.5 -N83 electrical error in the electric circuit

17614 einspritzventil Zyl.6 -N84 electrical error in the electric circuit

17615 einspritzventil Zyl.7 -N85 electrical error in the electric circuit

17616 einspritzventil Zyl.8 -N86 electrical error in the electric circuit

17621 einspritzventil Zyl.1 -N30 short-circuit after pluses

17622 einspritzventil Zyl.2 -N31 short-circuit after pluses

17623 einspritzventil Zyl.3 -N32 short-circuit after pluses

17624 einspritzventil Zyl.4 -N33 short-circuit after pluses

17625 einspritzventil Zyl.5 -N83 short-circuit after pluses

17626 einspritzventil Zyl.6 -N84 short-circuit after pluses

17627 einspritzventil Zyl.7 -N85 short-circuit after pluses

17628 einspritzventil Zyl.8 -N86 short-circuit after pluses

17633 einspritzventil Zyl. 1 -N30 short-circuit after mass

17634 einspritzventil Zyl. 2 -N31 short-circuit after mass

17635 einspritzventil Zyl. 3 -N32 short-circuit after mass

17636 einspritzventil Zyl. 4 -N33 short-circuit after mass

17637 einspritzventil Zyl. 5 -N83 short-circuit after mass

17638 einspritzventil Zyl. 6 -N84 short-circuit after mass

17639 einspritzventil Zyl. 7 -N85 short-circuit after mass

17640 einspritzventil Zyl. 8 -N86 short-circuit after mass

17645 einspritzventil Zyl. 1 -N30 interruption

17646 einspritzventil Zyl. 2 -N31 interruption

17647 einspritzventil Zyl. 3 -N32 interruption

17648 einspritzventil Zyl. 4 -N33 interruption

17649 einspritzventil Zyl. 5 -N83 interruption

17650 einspritzventil Zyl. 6 -N84 interruption

17651 einspritzventil Zyl. 7 -N85 interruption

17652 einspritzventil Zyl. 8 -N86 interruption

17658 Kraftstoffuellstand too small

17663 givers for coolant temperature -G62 short-circuit after mass

17664 givers for coolant temperature -G62 interruption/short-circuit after pluses

17668 valve for pump/nozzle cylinder 1 -N240 implausible signal

17669 valve for pump/nozzle cylinder 1 -N240 rule border exceeded

17670 valve for pump/nozzle cylinder 1 -N240 rule border fell below

17671 valve for pump/nozzle cylinder 2 -N241 implausible signal

17672 valve for pump/nozzle cylinder 2 -N241 rule border exceeded

17673 valve for pump/nozzle cylinder 2 -N241 rule border fell below

17674 valve for pump/nozzle cylinder 3 -N242 implausible signal

17675 valve for pump/nozzle cylinder 3 -N242 rule border exceeded

17676 valve for pump/nozzle cylinder 3 -N242 rule border fell below

17677 valve for pump/nozzle cylinder 4 -N243 implausible signal

17678 valve for pump/nozzle cylinder 4 -N243 rule border exceeded

17679 valve for pump/nozzle cylinder 4 -N243 rule border fell below

17686 valve for fuel dosage -N290 short-circuit after pluses

17687 valve for fuel dosage -N290 interruption/short-circuit after mass

17688 air distributor for einspritzventile throughput too small

17691 air distributor for einspritzventile of electrical errors in the electric circuit

17694 air distributor for einspritzventile short-circuit after pluses

17695 circulating air valve for turbocharger -N249 interruption

17696 circulating air valve for turbocharger -N249 short-circuit after pluses

17697 circulating air valve for turbocharger -N249 short-circuit after mass

17700 thermostat for characteristic diagram-steered engine cooling -F265 interruption

17701 thermostat for characteristic diagram-steered engine cooling -F265 short-circuit after pluses

17702 thermostat for characteristic diagram-steered engine cooling -F265 short-circuit after mass

17704 errors in the cooling system

17707 valve for fuel dosage -N290 malfunctioning

17708 burn misfires recognized reason: Lack of fuel

17709 knocking regulation Zyl. 9 rule border reaches

17710 knocking regulation Zyl. 10 rule border reaches

17711 knocking regulation Zyl. 11 rule border reaches

17712 knocking regulation Zyl. 12 rule border reaches

17713 ignition control Zyl. 9 interruption

17714 ignition control Zyl. 9 short-circuit after pluses

17715 ignition control Zyl. 9 short-circuit after mass

17716 ignition control Zyl. 10 interruption

17717 ignition control Zyl. 10 short-circuit after pluses

17718 ignition control Zyl. 10 short-circuit after mass

17719 ignition control Zyl. 11 interruption

17720 ignition control Zyl. 11 short-circuit after pluses

17721 ignition control Zyl. 11 short-circuit after mass

17722 ignition control Zyl. 12 interruption

17723 ignition control Zyl. 12 short-circuit after pluses

17724 ignition control Zyl. 12 short-circuit after mass

17729 knocking sensor 3 -G198 signal too small

17730 knocking sensor 3 -G198 signal too largely

17731 knocking sensor 4 -G199 signal too small

17732 knocking sensor 4 -G199 signal too largely

17733 knocking regulation Zyl. 1 rule border reaches

17734 knocking regulation Zyl. 2 rule border reaches

17735 knocking regulation Zyl. 3 rule border reaches

17736 knocking regulation Zyl. 4 rule border reaches

17737 knocking regulation Zyl. 5 rule border reaches

17738 knocking regulation Zyl. 6 rule border reaches

17739 knocking regulation Zyl. 7 rule border reaches

17740 knocking regulation Zyl. 8 rule border reaches

17743 engine moment monitoring rule border exceeded

17744 engine moment monitoring rule border exceeded

17745 bank 1, cam shaft position sensor -G40 short-circuit after mass

17746 bank 1, cam shaft position sensor -G40 interruption/short-circuit after pluses

17747 crankshaft position/engine speed sensor exchanges

17748 cam shaft position/crankshaft position sensor wrong allocation

17749 ignition exit 1 short-circuit after mass

17750 ignition exit 1 short-circuit after pluses

17751 ignition exit 2 short-circuit after mass

17752 ignition exit 2 short-circuit after pluses

17753 ignition exit 3 short-circuit after mass

17755 bank 2, cam shaft position crankshaft position sensor wrong allocation

17756 ignition exit 1 interruption

17757 ignition exit 2 interruption

17763 ignition control Zyl. 1 interruption

17764 ignition control Zyl. 1 short-circuit after pluses

17765 ignition control Zyl. 1 short-circuit after mass

17766 ignition control Zyl. 2 interruption

17767 ignition control Zyl. 2 short-circuit after pluses

17768 ignition control Zyl. 2 short-circuit after mass

17769 ignition control Zyl. 3 interruption

17770 ignition control Zyl. 3 short-circuit after pluses

17771 ignition control Zyl. 3 short-circuit after mass

17772 ignition control Zyl. 4 interruption

17773 ignition control Zyl. 4 short-circuit after pluses

17774 ignition control Zyl. 4 short-circuit after mass

17775 ignition control Zyl. 5 interruption

17776 ignition control Zyl. 5 short-circuit after pluses

17777 ignition control Zyl. 5 short-circuit after mass

17778 ignition control Zyl. 6 interruption

17779 ignition control Zyl. 6 short-circuit after pluses

17780 ignition control Zyl. 6 short-circuit after mass

17781 ignition control Zyl. 7 interruption

17782 ignition control Zyl. 7 short-circuit after pluses

17783 ignition control Zyl. 7 short-circuit after mass

17784 ignition control Zyl. 8 interruption

17785 ignition control Zyl. 8 short-circuit after pluses

17786 ignition control Zyl. 8 short-circuit after mass

17793 controller defectively

17794 controller defectively

17795 controller defectively

17796 controller defectively

17797 controller 2 for Diesel direct fuel injection system -J494 defectively

17799 bank 2 cam shaft position sensor -G40 short-circuit after mass

17800 bank 2 cam shaft position sensor -G40 interruption/short-circuit after pluses

17801 ignition exit 1 electrical error in the electric circuit

17802 ignition exit of 2 electrical errors in the electric circuit

17803 ignition exit 3 electrical error in the electric circuit

17805 giver wheel for engine speed adaptation border reaches

17806 engine speed signal, TD short-circuit after mass

17807 engine speed signal, TD short-circuit after pluses

17808 valve for recycling of exhaust gases -N18 of electrical errors in the electric circuit

17809 valve for recycling of exhaust gases -N18 short-circuit after mass

17810 valve for recycling of exhaust gases -N18 short-circuit after pluses

17811 recycling of exhaust gases system rule difference

17812 recycling of exhaust gases system basic adjustment not accomplished

17815 temperature sensors for recycling of exhaust gases -G98 signal too small

17816 temperature sensors for recycling of exhaust gases -G98 signal too largely

17817 tank ventilation valve -N80 of electrical errors in the electric circuit

17818 tank ventilation valve -N80 short-circuit after pluses

17819 bank 2, secondary air system throughput too small

17822 bank 2, secondary air system leakage recognized

17828 secondary air injecting valve -N112 of electrical errors in the electric circuit

17829 secondary air injecting valve -N112 short-circuit after mass

17830 secondary air injecting valve -N112 short-circuit after pluses

17831 bank 1, secondary air system throughput too small

17832 bank 1, secondary air system leakage recognized

17833 tank ventilation valve -N80 short-circuit after mass

17834 tank ventilation valve -N80 interruption

17840 secondary air injecting valve -N112 interruption

17841 relays for secondary tire pump -J299 interruption

17842 relays for secondary tire pump -J299 short-circuit after pluses

17843 relays for secondary tire pump -J299 short-circuit after mass

17844 relays for secondary tire pump -J299 of electrical errors in the electric circuit

17845 valve 2 for recycling of exhaust gases -N213 short-circuit after pluses

17846 valve 2 for recycling of exhaust gases -N213 interruption/short-circuit after mass

17847 potentiometers for recycling of exhaust gases -G212 error in basic adjustment

17848 valve for recycling of exhaust gases -N18 interruption

17849 valve for recycling of exhaust gases -N18 interruption/short-circuit after mass

17850 potentiometers for recycling of exhaust gases -G212 signal too largely

17851 potentiometers for recycling of exhaust gases -G212 signal too small

17858 secondary air system short-circuit after pluses

17859 secondary air system short-circuit after mass

17860 secondary air system interruption

17889 relays for secondary tire pump 2 -J545 interruption

17890 relays for secondary tire pump 2 -J545 short-circuit after pluses

17891 relays for secondary tire pump 2 -J545 short-circuit after mass

17892 relays for secondary tire pump 2 -J545 of electrical errors in the electric circuit

17893 secondary air injecting valve 2 -N320 interruption

17894 secondary air injecting valve 2 -N320 of electrical errors in the electric circuit

17895 secondary air injecting valve 2 -N320 short-circuit after mass

17896 secondary air injecting valve 2 -N320 short-circuit after pluses

17897 tank ventilation valve 2 -N333 short-circuit after pluses

17898 tank ventilation valve 2 -N333 short-circuit after mass

17899 tank ventilation valve 2 -N333 interruption

17900 tank ventilation valve 2 -N333 of electrical errors in the electric circuit

17902 tank ventilation system 2 throughput incorrectly

17908 fuel pump relays -J17 of electrical errors in the electric circuit

17909 fuel pump relays -J17 short-circuit after mass

17910 fuel pump relays -J17 short-circuit after pluses

17911 load signal of generator clamp DF implausible signal

17912 air intake system leakage recognized

not/interruption closes 17913 throttle idle microswitches -F60

not/short-circuit opens 17914 throttle idle microswitches -F60 after mass

17915 no-load operation system learning value lower limit reaches

17916 no-load operation system learning value upper border reaches

17917 valve for no-load operation stabilization -N71 of electrical errors in the electric circuit

17918 valve for no-load operation stabilization -N71 short-circuit after pluses

17919 valve for suction tube change-over -N156 of electrical errors in the electric circuit

17920 valve for suction tube change-over -N156 short-circuit after pluses

17921 valve 2 for suction tube change-over -N261 short-circuit after pluses

17922 valve 2 for suction tube change-over -N261 short-circuit after mass

17923 valve for suction tube change-over -N156 short-circuit after mass

17924 valve for suction tube change-over -N156 interruption

17925 main relays -J271 electrical error in the electric circuit

17926 main relays -J271 short-circuit after pluses

17927 bank 1, cam shaft adjustment malfunctioning

17928 valve 2 for suction tube change-over -N261 interruption

17930 bank 2, cam shaft adjustment malfunctioning

17931 Crash signal of the Airbag controller implausible signal

17932 fuel pump relays -J17 interruption/short-circuit after mass

17934 bank 1, cam shaft adjustment -N205 short-circuit after pluses

17935 bank 1, cam shaft adjustment -N205 short-circuit after mass

17936 bank 1, cam shaft adjustment -N205 interruption

17937 cam shaft adjustment short-circuit after pluses

17938 cam shaft adjustment short-circuit after mass

17939 cam shaft adjustment interruption

17942 bank 2, cam shaft adjustment -N208 short-circuit after pluses

17943 bank 2, cam shaft adjustment -N208 short-circuit after mass

17944 bank 2, cam shaft adjustment -N208 interruption

17947 clutch pedal switches -F36 implausible signal

17948 vehicle speed signal signal too largely

17949 fuel pump relays -J17 interruption

17950 angle sensors for butterfly valve drive -G187 implausible signal

17951 angle sensors for butterfly valve drive -G187 signal too small

17952 angle sensors for butterfly valve drive -G187 signal too largely

17953 butterfly valve control malfunctioning

17954 single solenoid valve for load pressure control -N75 short-circuit after pluses

17955 single solenoid valve for load pressure control -N75 short-circuit after mass

17956 single solenoid valve for load pressure control -N75 interruption

17957 single solenoid valve for load pressure control -N75 interruption/short-circuit after mass

17958 load pressure rule difference

17961 signal elevator giver/suction tube pressure implausible relationship

17962 butterfly valve control unit -J338 conditions for basic adjustment does not fulfill

17963 maximum load pressure exceeded

17964 load pressure control rule border fell below

17965 load pressure control rule border exceeded

17966 butterfly valve drive -G186 of electrical errors in the electric circuit

17967 butterfly valve control unit -J338 error in basic adjustment

17968 maximum engine speed exceeded

17972 butterfly valve control unit -J338 undervoltage during basic adjustment

17973 butterfly valve control unit -J338 lower notice one does not reach

17976 butterfly valve control unit -J338 of mechanical errors

17977 switches for GRA -E45 implausible signal

17978 engine expensive equipment closed

17979 valve left for engine storage -N144 short-circuit after pluses

17980 valve left for engine storage -N144 short-circuit after mass

17981 valve left for engine storage -N144 interruption

17982 valve left for engine storage -N144 of electrical errors in the electric circuit

17983 valve right for engine storage -N145 short-circuit after pluses

17984 valve right for engine storage -N145 short-circuit after mass

17985 valve right for engine storage -N145 interruption

17986 valve right for engine storage -N145 of electrical errors in the electric circuit

17987 butterfly valve control unit -J338 adaptation not started

17988 butterfly valve drive bank 1 malfunctioning

17989 butterfly valve control unit -J338 basic adjustment not accomplished

17990 no-load operation adaptation border reaches

17994 valves for engine storage -N144/-N145 short-circuit after pluses

18008 voltage supply Kl. 15 tension too small

18009 relays for voltage supply clamp 30 -J317 implausible signal

18010 voltage supply Kl.30 tension too small

18011 controller defectively

18012 controller defectively

18014 bad way info./engine target moment of the ABS controller of electrical errors in the electric circuit

18017 Crashabschaltung one released

18018 controller defectively

18019 requirement error lamp a short-circuit after mass

18020 engine expensive equipment wrongly codes

18023 givers for oil temperature -G8 implausible signal

18024 indicator light for time the glow plugs are on -K29 short-circuit after pluses

18025 indicator light for time the glow plugs are on -K29 interruption/short-circuit after mass

18026 relays for glow plugs -J52 short-circuit after pluses

18027 relays for glow plugs -J52 interruption/short-circuit after mass

18031 data bus drive no communication

18032 requirement error lamp actively

18033 data bus drive implausible message of the transmission expensive equipment

18034 data bus drive missing message of the transmission expensive equipment

18036 data bus drive missing message of the giver for guidance angles

18038 givers for position of the gas pedal -G79 signal too small

18039 givers for position of the gas pedal -G79 signal too largely

18040 givers for position of the gas pedal -G79 supply voltage

18041 givers 2 for position of the gas pedal -G185 signal too small

18042 givers 2 for position of the gas pedal -G185 signal too largely

18043 data bus drive missing message of the climatic expensive equipment

18044 data bus drive missing message of the Airbag controller

18045 data bus drive missing message of electronic central electrical connection

18047 givers 1/2 for position of the gas pedal -G79 and -G185 implausible signal

18048 controller defectively

18049 request error memory of the climatic expensive equipment select

18053 data bus drive missing message of the all wheel controller

18055 coding/variants of the controllers in the drive strand examine

18056 data bus drive defectively

18057 data bus drive missing message of the ABS controller

18058 data bus drive missing message of the combination instrument

18060 request error memory of the transmission expensive equipment select

18061 request error memory of the ABS controller select

18062 request error memory of the combination instrument select

18064 air conditioning system entrance/exit short-circuit after mass

18065 air conditioning system entrance/exit short-circuit after pluses

18067 radiator exhaust control 1 short-circuit after pluses

18068 radiator exhaust control 1 short-circuit after mass

18069 radiator exhaust control 2 short-circuit after pluses

18070 radiator exhaust control 2 short-circuit after mass

18071 control of valves pump/nozzle short-circuit after pluses

18072 control of valves pump/nozzle of electrical errors in the electric circuit

18073 control of valves pump/nozzle of mechanical errors

18074 valve for pump/nozzle cylinder 1 -N240 of electrical errors in the electric circuit

18075 valve for pump/nozzle cylinder 2 -N241 of electrical errors in the electric circuit

18076 valve for pump/nozzle cylinder 3 -N242 of electrical errors in the electric circuit

18077 valve for pump/nozzle cylinder 4 -N243 of electrical errors in the electric circuit

18080 radiator exhaust control 1 interruption/short-circuit after mass

18081 geschwindigkeitssignal error message of the ABS controller

18084 error lamp for electrical gas manipulation -K132 of electrical errors in the electric circuit

18085 error lamp for electrical gas manipulation -K132 short-circuit after pluses

18086 error lamp for electrical gas manipulation -K132 short-circuit after mass

18087 error lamp for electrical gas manipulation -K132 interruption

18089 controller programming of programming does not terminate

18090 data bus drive implausible message of the ABS controller

18098 error lamp for eigendiagnose -K83 of electrical errors in the electric circuit

18099 error lamp for eigendiagnose -K83 interruption

18100 error lamp for eigendiagnose -K83 short-circuit after mass

18101 error lamp for eigendiagnose -K83 short-circuit after pluses

18112 kickdown switches -F8 of electrical errors in the electric circuit

18132 signal for starter barrier short-circuit after mass

18137 signal for starter barrier short-circuit after pluses

18141 switches for Tiptronic, back -F189 short-circuit after mass

18147 switches for Tiptronic, highly -F189 short-circuit after mass

18148 clutch overloads

18149 clutch pressure adaptation adaptation border reaches

18150 clutch moment adaptation adaptation border reaches

18151 clutch slip monitoring signal too largely

18152 switches for Tiptronic, recognition -F189 short-circuit after mass

18153 Versorgungsspannnung for single solenoid valves short-circuit after pluses

18155 Versorgungsspannnung for single solenoid valves interruption/short-circuit after mass

18156 controller defectively

18157 controller for automatic transmission wrong coding

18158 voltage supply tension too small

18159 voltage supply tension too largely

18160 voltage supply implausible signal

18169 lock-out magnet -N110 short-circuit after mass

18170 lock-out magnet -N110 short-circuit after pluses

18171 lock-out magnet -N110 interruption

18172 transmission temperature monitoring

18179 load signal from the engine expensive equipment interruption/short-circuit after pluses

18180 load signal from the engine expensive equipment short-circuit after mass

18181 givers 1 for hydraulic pressure -G193 signal too largely

18192 high/back spacing line interruption/short-circuit after mass

18193 high/back spacing line short-circuit after pluses

18194 relays for back headlight interruption

18195 signal for back headlight short-circuit after mass

18196 signal for back headlight short-circuit after pluses

18198 signal for selecting range announcement interruption

18199 signal for selecting range announcement short-circuit after mass

18200 signal for selecting range announcement short-circuit after pluses

18201 givers 2 for transmission speed -G196 no signal

18203 signal for driving speed interruption

18204 signal for driving speed short-circuit after mass

18205 signal for driving speed short-circuit after pluses

18206 givers 2 for transmission speed -G196 implausible signal

18221 pressure control valve 1 -N215 of electrical errors in the electric circuit

18222 pressure control valve 1 -N215 interruption/short-circuit after mass

18223 pressure control valve 1 -N215 short-circuit after pluses

18226 pressure control valve 2 -N216 of electrical errors in the electric circuit

18227 pressure control valve 2 -N216 interruption/short-circuit after mass

18228 pressure control valve 2 -N216 short-circuit after pluses

18232 pressure control valve 3 -N216 interruption/short-circuit after mass

18233 pressure control valve 3 -N216 short-circuit after pluses

18237 pressure control valve 4 -N216 interruption/short-circuit after mass

18238 pressure control valve 4 -N216 short-circuit after pluses

18242 pressure control valve 5 -N216 interruption/short-circuit after mass

18243 pressure control valve 5 -N216 short-circuit after pluses

18249 engine/transmission expensive equipment variants does not fit

18256 request error memory of the engine expensive equipment select

18258 data bus drive missing message of the engine expensive equipment

18259 data bus drive missing message of the ABS controller

18261 data bus drive implausible message of the ABS controller

18262 data bus drive defectively

18263 data bus drive software condition monitoring (data bus drive)

18264 butterfly valve potentiometers -G69 error message of the engine expensive equipment

18265 load signal error message of the engine expensive equipment

18266 number of revolutions of the engine expensive equipment error message of the engine expensive equipment

18269 givers for position of the gas pedal -G79 error message of the engine expensive equipment

18308 radiator exhaust control 2 interruption/short-circuit after mass

18309 controller for radiator exhaust oh run -J138 short-circuit after pluses

18310 controller for radiator exhaust oh run -J138 interruption/short-circuit after mass

18311 valve for exhaust cooling agent -N313 short-circuit after pluses

18312 valve for exhaust cooling agent -N313 interruption/short-circuit after mass

18313 relays for pump load air cooling -J536 short-circuit after pluses

18314 relays for pump load air cooling -J536 interruption/short-circuit after mass

18315 data bus engine/engine defectively

18316 data bus engine/engine software condition monitoring

18317 data bus engine/engine missing message of the engine expensive equipment 1

18318 data bus engine/engine missing message of the engine expensive equipment 2

18319 Synchonisationsleitung engine/engine of electrical errors in the electric circuit

18328 valve for engine storage -N144/145 interruption/short-circuit after mass

18331 request error memory of the engine expensive equipment 2 select

18332 controller pin coding implausible signal

18333 relays for coolant additive pump -J496 short-circuit after pluses

18334 relays for coolant additive pump -J496 short-circuit after mass

18335 relays for coolant additive pump -J496 interruption

18342 temperature sensors for drive cycle radiator exhaust -G382 signal too small

18343 temperature sensors for drive cycle radiator exhaust -G382 signal too largely

19456 indicator light for time the glow plugs are on -K29

19458 kick-down switches -F8 implausible signal

19459 relays for small amount of heat -J359 short-circuit after pluses

19461 relays for large amount of heat -J360 short-circuit after pluses

19463 cam shaft position sensor -G40 no signal

19464 cam shaft position sensor -G40 signal outside of the tolerance

19465 relays for pump, fuel cooling -J445 short-circuit after pluses

19466 relays for pump, fuel cooling -J445 interruption/short-circuit after mass

19467 relays for electrical fuel pump 2 -J49 short-circuit after pluses

19468 relays for electrical fuel pump 2 -J49 interruption/short-circuit after mass

19469 valve 2 for load pressure control -N274 short-circuit after pluses

19470 valve 2 for load pressure control -N274 interruption/short-circuit after mass

19471 valve for fuel bypass -N312 short-circuit after pluses

19472 valve for fuel bypass -N312 interruption/short-circuit after mass

19473 valve for waste gas valve 1 -N321 short-circuit after pluses

19474 valve for waste gas valve 1 -N321 short-circuit after mass

19475 valve for waste gas valve 1 -N321 interruption

19476 valve for waste gas valve 1 -N321 of electrical errors in the electric circuit

19481 angle sensors 1 signal implausible for butterfly valve drive 2 -G297

19482 angle sensors 1 for butterfly valve drive 2 -G297 signal too small

19483 angle sensors 1 for butterfly valve drive 2 -G297 signal too largely

19484 angle sensors 2 for butterfly valve drive 2 -G298 implausible signal

19485 angle sensors 2 for butterfly valve drive 2 -G298 signal too small

19486 angle sensors 2 for butterfly valve drive 2 -G298 signal too largely

19487 butterfly valve drive 2 -G296 of electrical errors in the electric circuit

19488 butterfly valve control unit 2 -J544 errors in basic adjustment

19489 givers 2 for intake air temperature -G299 signal too small

19490 givers 2 for intake air temperature -G299 signal too largely

19491 butterfly valve control unit 2 -J544 of mechanical errors

19492 butterfly valve control unit 2 -J544 undervoltage during basic adjustment

19493 butterfly valve control unit 2 -J544 adaptation not started

19494 butterfly valve control unit 2 -J544 lower notice one does not reach

19560 transfer valve for suction tube flap -N239 short-circuit after pluses

19561 transfer valve for suction tube flap -N239 interruption/short-circuit after mass

19656 exhaust bank 3, probe 1 heizstromkreis short-circuit after mass

19657 exhaust bank 3, probe 1 heizstromkreis short-circuit after pluses

19658 exhaust bank 3, probe 1 heizstromkreis interruption

19659 exhaust bank 3, probe 1 heizstromkreis of electrical errors

19662 exhaust bank 3, probe 1 tension too largely

19663 exhaust bank 3, probe 1 electrical error in the electric circuit

19664 exhaust bank 3, probe 1 no activity

19665 exhaust bank 3, probe 1 signal too slowly

19666 exhaust bank 3, probe 1 heizstromkreis achievement too small

19671 exhaust bank 3, probe 2 heizstromkreis short-circuit after mass

19672 exhaust bank 3, probe 2 heizstromkreis short-circuit after pluses

19673 exhaust bank 3, probe 2 heizstromkreis interruption

19674 exhaust bank 3, probe 2 heizstromkreis of electrical errors

19675 exhaust bank 3, probe 2 internal resistance too largely

19676 exhaust bank 3, probe 2 tension too small

19677 exhaust bank 3, probe 2 tension too largely

19678 exhaust bank 3, probe 2 electrical error in the electric circuit

19679 exhaust bank 3, probe 2 no activity

19680 exhaust bank 3, probe 2 signal too slowly

19686 exhaust bank 4, probe 1 heizstromkreis short-circuit after mass

19687 exhaust bank 4, probe 1 heizstromkreis short-circuit after pluses

19688 exhaust bank 4, probe 1 heizstromkreis interruption

19689 exhaust bank 4, probe 1 heizstromkreis of electrical errors

19692 exhaust bank 4, probe 1 tension too largely

19693 exhaust bank 4, probe 1 electrical error in the electric circuit

19694 exhaust bank 4, probe 1 no activity

19695 exhaust bank 4, probe 1 signal too slowly

19696 exhaust bank 4, probe 1 heizstromkreis achievement too small

19701 exhaust bank 4, probe 2 heizstromkreis short-circuit after mass

19702 exhaust bank 4, probe 2 heizstromkreis short-circuit after pluses

19703 exhaust bank 4, probe 2 heizstromkreis interruption

19704 exhaust bank 4, probe 2 heizstromkreis electrical error

19705 exhaust bank 4, probe 2 internal resistance too largely

19706 exhaust bank 4, probe 2 tension too small

19707 exhaust bank 4, probe 2 tension too largely

19708 exhaust bank 4, probe 2 electrical error in the electric circuit

19709 exhaust bank 4, probe 2 no activity

19710 exhaust bank 4, probe 2 signal too slowly

19716 exhaust bank 1/2 Lambda probes before Kat exchanges

19717 exhaust bank 3/4 Lambda probes before Kat exchanges

19718 exhaust bank 1/2 Lambda probes after Kat exchanges

19719 exhaust bank 3/4 Lambda probes after Kat exchanges

19720 Vorkatalysator exhaust bank 3 effect too small

19721 Vorkatalysator exhaust bank 4 effect too small

19756 bank 1, cam shaft position sensor, discharge opening -G300 short-circuit after mass

19757 bank 1, cam shaft position sensor, discharge opening -G300 interruption/short-circuit after pluses

19758 bank 2, cam shaft position sensor, discharge opening -G301 short-circuit after mass

19759 bank 2, cam shaft position sensor, discharge opening -G301 interruption/short-circuit after pluses

19760 bank 1, exhaust cam wave position sensor -G300/crankshaft position sensor -G28 wrong allocation

19761 bank 2, exhaust cam wave position sensor -G301/crankshaft position sensor -G28 wrong allocation

65535 controller defectively

-------------------------------------------------------------------------------

Error kinds:

01-00 short-circuit after pluses

02-00 short-circuit after mass

03-00 no signal

04-00 mechanical error

05-00 entrance openly

06-00 signal too largely

07-00 signal too small

08-00 rule border exceeded

09-00 adaptation border exceeded

10-00 adaptation border fell below

11-00 rule border fell below

12-00 adaptation border (mul.) exceeded

13-00 adaptation border (mul.) fallen below

14-00 adaptation border (ADD.) exceeded

15-00 adaptation border (ADD.) fallen below

16-00 signal outside of the tolerance

17-00 rule difference

18-00 upper notice value

19-00 lower notice value

20-00 errors in basic adjustment

21-00 time for pressure build-up in front too long

22-00 time for pressure drop in front too long

23-00 time for pressure build-up in the back too long

24-00 time for pressure drop in the back too long

25-00 undefined switch condition

26-00 exit openly

27-00 implausible signal

28-00 short-circuit after pluses

29-00 short-circuit after mass

30-00 interruption/short-circuit after pluses

31-00 interruption/short-circuit after mass

32-00 resistance value too largely

33-00 resistance value too small

34-00 no error recognized

35-00

36-00 interruption

37-00 defectively

/ short-circuit does not switch 38-00 exit after pluses

/ short-circuit does not switch 39-00 exit after mass

40-00 short-circuit to other valve

41-00 blocks or without tension

42-00 number of revolutions deviation too largely

43-00 closed

44-00 short-circuit

45-00 patch cord

46-00 leaky

47-00 wrongly attached

48-00 voltage supply

49-00 no communication

50-00 position early does not reach

51-00 position late does not reach

52-00 voltage supply too largely

53-00 voltage supply too small

54-00 wrong equipment

55-00 adaptation does not take place

56-00 in the fail-safe

57-00 electrical error in the electric circuit

58-00 does not lock

59-00 does not unlock

60-00 safed not

61-00 entsafed not

62-00 no or wrong attitude

63-00 temperature disconnection

67-00 desired value does not reach

68-00 cylinders 1

69-00 cylinders 2

70-00 cylinders 3

71-00 cylinders 4

72-00 cylinders 5

73-00 cylinders 6

74-00 cylinders 7

75-00 cylinders 8

is missing to 76-00 clamp 30

77-00 internal voltage supply

78-00 missing messages

79-00 please error memory select

80-00 in the single-wire enterprise

81-00 openly

82-00 released

192-00 at present not controllably

193-00 not entitled

194-00 alignment not accomplished